## Slide 1
Constructive Computer Architecture:
Branch Prediction
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Control Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
  Loop length x pipeline width
What fraction of executed instructions are branch instructions?
superscalarity

## Slide 4: How frequent are branches?
Blem et al [HPCA 2013] Spec INT 2006 on ARM Cortex 7
 | ARM Cortex-A9; ARMv7 ISA |  |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
astar | 1.47E+10 | 16.0 | 55.6 | 13.0 | 15.4
bzip2 | 2.41E+10 | 8.7 | 34.6 | 14.4 | 42.2
gcc | 5.61E+09 | 10.2 | 19.1 | 11.2 | 59.5
gobmk | 5.75E+10 | 10.7 | 25.4 | 7.2 | 56.8
hmmer | 1.56E+10 | 5.1 | 41.8 | 18.1 | 35.0
h264 | 1.06E+11 | 5.5 | 30.4 | 10.4 | 53.6
libquantum | 3.97E+08 | 11.5 | 8.1 | 11.7 | 68.7
omnetpp | 2.67E+09 | 11.7 | 19.3 | 8.9 | 60.1
perlbench | 2.69E+09 | 10.7 | 24.6 | 9.3 | 55.5
sjeng | 1.34E+10 | 11.5 | 39.3 | 13.7 | 35.5
Average |  | 8.2 | 31.9 | 10.9 | 49.0
Every 12th instruction is a branch

## Slide 5: How frequent are branches?
Blem et al [HPCA 2013] Spec FP 2006 on ARM Cortex 7
 | ARM Cortex-A9; ARMv7 ISA |  |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
bwaves | 3.84E+11 | 13.5 | 1.4 | 0.5 | 84.7
cactusADM | 1.02E+10 | 0.5 | 51.4 | 17.9 | 30.1
leslie3D | 4.92E+10 | 6.2 | 2.0 | 3.7 | 88.1
milc | 1.38E+10 | 6.5 | 38.2 | 13.3 | 42.0
tonto | 1.30E+10 | 10.0 | 40.5 | 14.1 | 35.4
Average |  | 12.15 | 4.68 | 1.95 | 81.22
Every 8th instruction is a branch

## Slide 6: How frequent are branches?
 |  | core i7; x86 ISA |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
astar | 5.71E+10 | 6.9 | 19.5 | 6.9 | 66.7
bzip2 | 4.25E+10 | 11.1 | 31.2 | 11.8 | 45.9
hmmer | 2.57E+10 | 5.3 | 30.5 | 9.4 | 54.8
gcc | 6.29E+09 | 15.1 | 22.1 | 14.1 | 48.7
gobmk | 8.93E+10 | 12.1 | 21.7 | 13.4 | 52.7
h264 | 1.09E+11 | 7.1 | 46.8 | 18.5 | 27.6
libquantum | 4.18E+08 | 13.2 | 39.3 | 6.8 | 40.7
omnetpp | 2.55E+09 | 16.4 | 28.6 | 21.4 | 33.7
perlbench | 2.91E+09 | 17.3 | 25.9 | 16.0 | 40.8
sjeng | 2.11E+10 | 14.8 | 22.8 | 11.0 | 51.4
Average |  | 9.4 | 31.0 | 13.4 | 46.2
Blem et al [HPCA 2013] Spec INT 2006 on X86
Every 10th or 11th instruction is a branch

## Slide 7: How frequent are branches?
Blem et al [HPCA 2013] Spec FP 2006 on X86
 |  | core i7; x86 ISA |  |  | 
Benchmark | Total Instructions | branch % | load % | store % | other %
bwaves | 3.41E+10 | 3.2 | 51.4 | 16.8 | 28.7
cactusADM | 1.05E+10 | 0.4 | 55.3 | 18.6 | 25.8
leslie3D | 6.25E+10 | 4.9 | 35.3 | 12.8 | 46.9
milc | 3.29E+10 | 2.2 | 32.2 | 13.8 | 51.8
tonto | 4.88E+09 | 7.1 | 27.2 | 12.4 | 53.3
Average |  | 3.6 | 39.6 | 14.4 | 42.4
Every 27th instruction is a branch

## Slide 8: Observations
No pipelined processor can work without a next address prediction
Control transfer happens every 8th to 30th instruction

## Slide 9: Simplest Next Address Prediction (NAP)
What is it?
Is this a good idea?
Can we do better?
pc, pc+4, pc+8, …i.e., Jumps and Branch are predicted not taken
Yes, by knowing something about the program or by learning from the past behavior of the program, aka dynamic branch prediction
yes, because most instructions are not control transfer instructions (reported 70% accuracy)

## Slide 10: Static Branch Prediction
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64
  reported as ~80% accurate
Overall probability a branch is taken is ~60-70% but:
JZ
JZ
backward
90%
forward
50%
... but our ISA is fixed!

## Slide 11: Dynamic Branch Prediction
pc
Truth/Feedback
Prediction
Predictor
Operations
  Predict
  Update
update
predict

## Slide 12: Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 13: Observations
There is a plethora of branch prediction schemes – their importance grows with the depth of processor pipeline
Processors often use more than one prediction scheme
It is usually easy to understand the data structures required to implement a particular scheme
It takes considerably more effort to
  Integrate a prediction scheme in the pipeline
  Understand the interactions between various schemes
  Understand the performance implications
we will start with the basics ...

## Slide 14: MIPS Branches and Jumps
Instruction Direction known after Target known after
J
JR
BEQZ/BNEZ
Each instruction fetch depends on some information from the preceding instruction:
1. Is the preceding instruction a taken branch?
2. If so, what is the target address?
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Reg. Fetch
After Exec
A predictor can redirect the pc only after the relevant information required by the predictor is available

## Slide 15: Overview of control prediction
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
Given (pc, ppc), a misprediction can be corrected (used to redirect the pc) as soon as it is detected. In fact, pc can be redirected as soon as we have a “better” prediction. However, for forward progress it is important that a correct pc should never be redirected.
mispred insts must be filtered
correct mispred
correct mispred
correct mispred
Notes: With respect to branches the important steps are…
With ‘stall style’ dependence resolution - correct next PC calculation waits for …
To alleviate stalls speculate next PC – now dependence info is speculation check

## Slide 16: Next Address Predictor (NAP) first attempt
Fetch: ppc = look up the target in BTB
Later check prediction, if wrong then kill the instruction
and update BTB
iMem
pc
Branch Target
Buffer (BTB)
(2k entries)
k
predicted
target
target
pc is the only information NAP has

## Slide 17: Address Collisions
What will be fetched after the instruction at 1028?
NAP prediction =
Correct target =

Assume a
128-entry
BTB
target
236
1028 Add .....
132 Jump 100
Instruction
Memory
236
1032
kill PC=236 and fetch PC=1032
Is this a common occurrence?
Can we avoid these bubbles?
yes
yes

## Slide 18: Use BTB for Control Instructions only
BTB contains useful information for branch and jump instructions only
 Do not update it for other instructions
For all other instructions the next PC is (PC)+4!
How to achieve this effect without decoding the instruction?

## Slide 19: Branch Target Buffer (BTB)
Keep the (pc, target pc) in the BTB
pc+4 is predicted if no pc match is found
BTB is updated only for branches and jumps
2k-entry direct-mapped BTB
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC
Permits ppc to be determined before instruction is decoded

## Slide 20: Consulting BTB Before Decoding
1028 Add .....
132 Jump 100
target
236
entry PC
132
If the match for pc fails, pc+4 is fetched
  pc=132, match succeeds, instruction at 236 is fetched
  pc=1028, match fails, instruction at 1028+4 is fetched
 eliminates false predictions after ALU instructions
BTB contains entries only for control transfer instructions
   more room to store branch targets
Even very small BTBs are very effective

## Slide 21: Next Addr Predictor interface
interface AddrPred; method Addr predPc(Addr pc); method Action update(Redirect rd); endinterface
Two implementations:
Simple PC+4 predictor
Predictor using BTB

## Slide 22: Simple PC+4 predictor
module mkPcPlus4(AddrPred); method Addr predPc(Addr pc);
return pc + 4;
endmethod
method Action update(Redirect rd); endmethod endmodule

## Slide 23: BTB predictor
module mkBtb(AddrPred); RegFile#(BtbIndex, Addr) ppcArr <- mkRegFileFull; RegFile#(BtbIndex, BtbTag) entryPcArr <- mkRegFileFull; Vector#(BtbEntries, Reg#(Bool))
validArr <- replicateM(mkReg(False));
function BtbIndex getIndex(Addr pc)=truncate(pc>>2); function BtbTag getTag(Addr pc) = truncateLSB(pc);
method Addr predPc(Addr pc); BtbIndex index = getIndex(pc); BtbTag tag = getTag(pc); if(validArr[index] && tag == entryPcArr.sub(index)) return ppcArr.sub(index); else return (pc + 4); endmethod
method Action update(Redirect redirect); ...
endmodule

## Slide 24: BTB predictor update method
method Action update(Redirect redirect);
if(redirect.taken)
begin let index = getIndex(redirect.pc); let tag = getTag(redirect.pc);
validArr[index] <= True; entryPcArr.upd(index, tag); ppcArr.upd(index, redirect.nextPc);
end endmethod
Input redirect contains pc, the correct next pc and
whether the branch was taken or not (to avoid making
entries for not-taken branches

## Slide 25: Integrating BTB in the 2-Stage pipeline
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(Decode2Execute) d2e <- mkFifo;
Reg#(Bool) fEpoch <- mkReg(False);
Reg#(Bool) eEpoch <- mkReg(False);
Fifo#(Addr) redirect <- mkFifo;
AddrPred btb <- mkBtb
Scoreboard#(1) sb <- mkScoreboard;
rule doFetch …
rule doExecute …
Notes: 25

## Slide 26: 2-Stage-DH pipeline doFetch rule
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first;
redirect.deq; end
else begin let ppc = nextAddrPredictor(pc); let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, nextPC: ppc,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); pc <= ppc; end
end
endrule
update btb
btb.predPc(pc)
change pc only on a mispredict
btb.update(redirect.first); redirect.deq; end
if(redirect.notEmpty && redirect.first.mispredict)
begin pc <= redirect.first.ppc; fEpoch <= !fEpoch; end

## Slide 27: 2-Stage-DH pipeline doExecute rule
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin redirect.enq(eInst.addr); eEpoch <= !eEpoch; end end d2e.deq; sb.remove; endrule
send information about branch resolution
if(eInst.iType == J || eInst.iType == Jr || eInst.iType == Br) redirect.enq(Redirect{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken, mispredict: eInst.mispredict,
brType: eInst.iType, }); if(eInst.mispredict) eEpoch <= !eEpoch; d2e.deq; sb.remove; endrule

## Slide 28: Multiple Predictors: BTB + Branch Direction Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
correct mispred
correct mispred
stay tuned