## Slide 1
Constructive Computer Architecture:
Branch Prediction:
Direction Predictors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Multiple Predictors: BTB + Branch Direction Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
correct mispred
correct mispred

## Slide 4: Branch Prediction Bits Remember how the branch was resolved previously
Assume 2 BP bits per instruction
Use saturating counter
On ¬taken  |  On taken | 1 | 1 | Strongly taken
 |  | 1 | 0 | Weakly taken
 |  | 0 | 1 | Weakly ¬taken
 |  | 0 | 0 | Strongly ¬taken
Direction prediction changes only after two successive bad predictions

## Slide 5: Two-bit versus one-bit Branch prediction
Consider the branch instruction needed to implement a loop
  with one bit, the prediction will always be set incorrectly on loop exit
  with two bits the prediction will not change on loop exit
A little bit of hysteresis is good in changing predictions

## Slide 6: Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct direction predictions
0
0
Fetch PC
Branch?
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?
Target PC
+
from Fetch
After decoding the instruction if it turns out to be a branch, then we can consult BHT using the pc; if this prediction is different from the incoming ppc we can redirect Fetch

## Slide 7: Where does BHT fit in the processor pipeline?
BHT can only be used after instruction decode
We still need the next instruction address predictor (e.g., BTB) at the fetch stage
Need a mechanism to update the BHT
  where does the update information come from?
Execute

## Slide 8: A step-by-step explanation of how pipelines with multiple predictors work

## Slide 9: N-Stage pipeline – BTB only
recirect
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
fEpoch
At Execute:
  if (epoch!=eEpoch) then mark instruction as poisoned, send it to the latter stages so that scoreboard entry can be removed
  if no poisoning & mispred then change eEpoch; send <pc, newPc, ...> to Fetch
At Fetch:
  msg from execute: train BTB with <pc, newPc, taken, mispredict>
  if msg from execute indicates misprediction then set pc, change fEpoch
attached to every fetched instruction
{pc, ppc, epoch}
eEpoch
{pc, newPc, taken mispredict, ...}
BTB
...
Notes: 9
In a similar way to FXep and Xep, we distribute Dep into Dep and FDep.

## Slide 10: Nomenclature
Drop an instruction: What we really mean is poison the instruction so that the subsequent stages know not to update any architectural state. The poisoned instruction has to be passed down for book keeping reasons, i.e., to remove it from the scoreboard.
Detecting a misprediction versus training/updating a predictor. On a pc misprediction, information about redirecting the pc has to be passed to the fetch stage. However for training the BTB and other predictors information has to be passed even when there is no misprediction.
  we will first focus on pc redirection and then on predictor training

## Slide 11: N-Stage pipeline: Two predictors
Suppose both Decode and Execute can redirect the PC; Execute redirect should have priority, i.e., Execute redirect should never be overruled
We will use separate epochs for each redirecting stage
  feEpoch and deEpoch are estimates of eEpoch at Fetch and Decode, respectively
  fdEpoch is Fetch’s estimates of dEpoch
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
redirect PC
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...

## Slide 12: N-Stage pipeline: Two predictors Redirection logic
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...
At execute:
  if (ieEp!=eEp) then drop the instruction
  if no-drop & mispred then change eEp; send <correct next pc, new eEp, …> to fetch
At fetch:
  msg from execute: if (mispredict) set pc, change feEp
  msg from decode: if (ideEp=feEp)then set pc, change fdEp
At decode:
  if (ieEp!=deEp) then deEp <= ieEp and dEp = idEp
  else if (idEp!=dEp) then drop the instruction
  for non dropped instructions
  if (ppc != Dpred(pc)) then change dEp, send <Dpred(pc), new dEp, deEp> to Fetch
{..., ieEp}
{pc, ppc, ieEp, idEp}
{pc, newPc, taken mispredict, ...}
{pc, newPc, idEp, ideEp...}
make sure that the msg from Decode is not from a wrong path instruction
if incoming eEp does not match deEp then Execute has redirected the pc

## Slide 13: now some coding ...
4-stage pipeline (F, D&R, E&M, W)
No predictor training, so messages are sent only for redirection
You will explore the effect of predictor training in the lab

## Slide 14: 4-Stage pipeline with Branch Prediction
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(1, Decode2Execute) d2e <- mkPipelineFifo;
Fifo#(1, Exec2Commit) e2c <- mkPipelineFifo;
Scoreboard#(2) sb <- mkPipelineScoreboard;
Reg#(Bool) feEp <- mkReg(False);
Reg#(Bool) fdEp <- mkReg(False);
Reg#(Bool) dEp <- mkReg(False);
Reg#(Bool) deEp <- mkReg(False);
Reg#(Bool) eEp <- mkReg(False);
Fifo#(ExecRedirect) redirect <- mkBypassFifo;
Fifo#(DecRedirect) decRedirect <- mkBypassFifo;
AddrPred#(16) addrPred <- mkBTB;
DirPred#(1024) dirPred <- mkBHT;
Notes: 14

## Slide 15: 4-Stage-BP pipeline Fetch rule
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty) begin feEp <= !feEp; pc <= redirect.first.newPc;
redirect.deq; end else if(decRedirect.notEmpty)
begin
if(decRedirect.first.eEp == feEp) begin
fdEp <= !fdEp; pc <= decRedirect.first.newPc; end
decRedirect.deq;
end;
else begin let ppc = addrPred.predPc(pc);
f2d.enq(Fetch2Decoode{pc: pc, ppc: ppc, inst: inst,
eEp: feEp, dEp: fdEp});
end
endrule

## Slide 16: 4-Stage-BP pipeline Decode&RegRead Action
function Action decAndRegFetch(DInst dInst, Addr pc, Addr ppc, Bool eEp);
action let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2)
|| sb.search3(dInst.dst);;
if(!stall)
begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppc,
dInst: dInst, epoch: eEp,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst);
end
endaction
endfunction

## Slide 17: 4-Stage-BP pipeline Decode&RegRead rule
rule doDecode;
let x = f2d.first; let inst = x.inst; let pc = x.pc;
let ppc = x.ppc; let idEp = x.dEp; let ieEp = x.eEp;
let dInst = decode(inst);
let newPc = dirPrec.predAddr(pc, dInst);
if(ieEp != deEp) begin // change Decode’s epochs and
// continue normal instruction execution
deEp <= ieEp; let newdEp = idEp;
decAndRegRead(inst, pc, newPc, ieEp);
if(ppc != newPc) begin
newDEp = !newdEp; decRedirect.enq(DecRedirect{pc: pc,
newPc: newPc, eEp: ieEp}); end
dEp <= newdEp end
else if(idEp == dEp) begin decAndRegRead(inst, pc, newPc, ieEp);
if(ppc != newPc) begin
dEp <= !dEp; decRedirect.enq(DecRedirect{pc: pc,
newPc: newPc, eEp: ieEp}); end
end
f2d.deq; endrule

## Slide 18: 4-Stage-BP pipeline Execute rule
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); e2c.enq(Exec2Commit{dst:eInst.dst, data:eInst.data}); if(eInst.mispredict) begin redirect.enq(eInst.addr); eEpoch <= !eEpoch; end end
else e2c.enq(Exec2Commit{dst:Invalid, data:?}); d2e.deq; endrule
no change

## Slide 19: 4-Stage-BP pipeline Commit rule
rule doCommit;
let dst = eInst.first.dst;
let data = eInst.first.data;
if(isValid(dst))
rf.wr(tuple2(validValue(dst), data);
e2c.deq;
sb.remove;
endrule
no change
Notes: 19

## Slide 20: Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor and the predictor uses this information to predict the resolution of the next branch
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition is false then so is second condition

## Slide 21: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Taken/¬Taken?
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Four
2k, 2-bit
Entry
BHT

## Slide 22: Uses of Jump Register (JR)
Switch statements (jump to address of matching case)
Dynamic function call (jump to run-time function address)
Subroutine returns (jump to return address)
How well does BTB work for each of these cases?
BTB works well if the same case is used repeatedly
BTB works well if the same function is usually called, (e.g., in C++ programming, when objects have same type in virtual function call)
BTB works well if usually return to the same place
However, often one function is called from many distinct call sites!

## Slide 23: Subroutine Return Stack
A small structure to accelerate JR for subroutine returns is typically much more accurate than BTBs
&fb()
&fc()
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
&fd()
k entries
(typically k=8-16)
Pop return address when subroutine return decoded
Push call address when function call executed

## Slide 24: Multiple Predictors: BTB + BHT + Ret Predictors
One of the PowerPCs has all the three predictors
Performance analysis is quite difficult – depends upon the sizes of various tables and program behavior
Correctness: The system must work even if every prediction is wrong
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
Ret Addr stack JR
correct mispred