## Slide 1
Constructive Computer Architecture:
Branch Prediction:
Direction Predictors
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Slides from L15 are included for completeness sake

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Multiple Predictors: BTB + Branch Direction Predictors
Suppose we maintain a table of how a particular Br has resolved before. At the decode stage we can consult this table to check if the incoming (pc, ppc) pair matches our prediction. If not redirect the pc
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
correct mispred
correct mispred

## Slide 4: Branch Prediction Bits Remember how the branch was resolved previously
Assume 2 BP bits per instruction
Use saturating counter
On ¬taken  |  On taken | 1 | 1 | Strongly taken
 |  | 1 | 0 | Weakly taken
 |  | 0 | 1 | Weakly ¬taken
 |  | 0 | 0 | Strongly ¬taken
Direction prediction changes only after two successive bad predictions

## Slide 5: Two-bit versus one-bit Branch prediction
Consider the branch instruction needed to implement a loop
  with one bit, the prediction will always be set incorrectly on loop exit
  with two bits the prediction will not change on loop exit
A little bit of hysteresis is good in changing predictions

## Slide 6: Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct direction predictions
0
0
Fetch PC
Branch?
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?
Target PC
+
from Fetch
After decoding the instruction if it turns out to be a branch, then we can consult BHT using the pc; if this prediction is different from the incoming ppc we can redirect Fetch

## Slide 7: Where does BHT fit in the processor pipeline?
BHT can only be used after instruction decode
We still need the next instruction address predictor (e.g., BTB) at the fetch stage
Predictor training: On a pc misprediction, information about redirecting the pc has to be passed to the fetch stage. However for training branch predictors information has to be passed even when there is no misprediction

## Slide 8: 2-Stage-DH pipeline doExecute rule
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin redirect.enq(RedirectInfo{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken);
eEpoch <= !eEpoch; end end d2e.deq; sb.remove; endrule
Even if there is no misprediction, send information about branch resolution for training predictors

## Slide 9: 2-Stage-DH pipeline doExecute rule: predictor training
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data); if(eInst.mispredict) begin redirect.enq(RedirectInfo{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken);
eEpoch <= !eEpoch; end end d2e.deq; sb.remove; endrule
Even if there is no misprediction, send information about branch resolution for training predictors
if(eInst.mispredict) eEpoch <= !eEpoch;
if(eInst.iType == J || eInst.iType == Jr || eInst.iType == Br) redirect.enq(Redirect{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken, mispredict: eInst.mispredict,
brType: eInst.iType}); d2e.deq; sb.remove; endrule

## Slide 10: 2-Stage-DH pipeline doFetch rule:
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first.nextPC;
redirect.deq; nap.update(redirect.first); end
else begin let ppc = nap.predPC(pc); let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, nextPC: ppc,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); pc <= ppc; end
end
endrule
update nap but change pc only on a mispredict

## Slide 11: 2-Stage-DH pipeline doFetch rule: predictor training
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty) begin fEpoch <= !fEpoch; pc <= redirect.first.nextPc;
redirect.deq; nap.update(redirect.first); end
else begin let ppc = nap.predPC(pc); let dInst = decode(inst);
let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall) begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, nextPC: ppc,
dIinst: dInst, epoch: fEpoch,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst); pc <= ppc; end
end
endrule
update nap but change pc only on a mispredict
if(redirect.notEmpty && redirect.first.mispredict)
begin pc <= redirect.first.nextPc; fEpoch <= !fEpoch; end

## Slide 12: Multiple predictors in a pipeline
At each stage we need to take two decisions:
  Whether the current instruction is a wrong path instruction. Requires looking at epochs
  Whether the prediction (ppc) following the current instruction is good or not. Requires consulting the prediction data structure (BTB, BHT, …)
Fetch stage must correct the pc unless the redirection comes from a known wrong path instruction
Redirections from Execute stage are always correct, i.e., cannot come from wrong path instructions

## Slide 13: Dropping or poisoning an instruction
Once an instruction is determined to be on the wrong path, the instruction is either dropped or poisoned
Drop: If the wrong path instruction has not modified any book keeping structures (e.g., Scoreboard) then it is simply removed
Poison: If the wrong path instruction has modified book keeping structures then it is poisoned and passed down for book keeping reasons (say, to remove it from the scoreboard)
Subsequent stages know not to update any architectural state for a poisoned instruction

## Slide 14: N-Stage pipeline – BTB only
recirect
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
fEpoch
At Execute:
  (pc) if (epoch!=eEpoch) then mark instruction as poisoned
  (ppc) if (no poisoning) & mispred then change eEpoch; send <pc, newPc, ...> to Fetch
At Fetch:
  msg from execute: train BTB with <pc, newPc, taken, mispredict>
  if msg from execute indicates misprediction then set pc, change fEpoch
attached to every fetched instruction
{pc, ppc, epoch}
eEpoch
{pc, newPc, taken mispredict, ...}
BTB
...
Notes: 14
In a similar way to FXep and Xep, we distribute Dep into Dep and FDep.

## Slide 15: N-Stage pipeline: Two predictors
Suppose both Decode and Execute can redirect the PC; Execute redirect should have priority, i.e., Execute redirect should never be overruled
We will use separate epochs for each redirecting stage
  feEpoch and deEpoch are estimates of eEpoch at Fetch and Decode, respectively
  fdEpoch is Fetch’s estimates of dEpoch
  Initially set all epochs to 0
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
redirect PC
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...

## Slide 16: N-Stage pipeline: Two predictors Redirection logic
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...
At execute:
  (pc) if (ieEp!=eEp) then poison the instruction
  (ppc) if (no poisoning) & mispred then change eEp;
  (ppc) for every control instruction send <pc, target pc, taken, mispred…> to fetch
At fetch:
  msg from execute: if (mispred) set pc, change feEp,
  msg from decode: If (no redirect message from Execute)
  if (ideEp=feEp) then set pc, change fdEp to idEp
At decode: …
{..., ieEp}
{pc, ppc, ieEp, idEp}
{pc, newPc, taken mispredict, ...}
{pc, newPc, idEp, ideEp...}
make sure that the msg from Decode is not from a wrong path instruction

## Slide 17: Decode stage Redirection logic
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...
{..., ieEp}
{pc, ppc, ieEp, idEp}
{pc, newPc, taken mispredict, ...}
{pc, newPc, idEp, ideEp...}
Is ieEp = deEp ?
Is idEp = dEp ?
Current instruction is OK but
Execute has redirected the pc;
Set <deEp, dEp> to <ieEp, idEp>
check the ppc prediction via BHT,
Switch dEp if misprediction
yes
no
yes
no
Current instruction is OK; check the ppc prediction via BHT, Switch dEp if misprediction
Wrong path instruction; drop it

## Slide 18: now some coding ...
4-stage pipeline (F, D&R, E&M, W)
Direction predictor training is incompletely specified
You will explore the effect of predictor training in the lab

## Slide 19: 4-Stage pipeline with Branch Prediction
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(1, Decode2Execute) d2e <- mkPipelineFifo;
Fifo#(1, Exec2Commit) e2c <- mkPipelineFifo;
Scoreboard#(2) sb <- mkPipelineScoreboard;
Reg#(Bool) feEp <- mkReg(False);
Reg#(Bool) fdEp <- mkReg(False);
Reg#(Bool) dEp <- mkReg(False);
Reg#(Bool) deEp <- mkReg(False);
Reg#(Bool) eEp <- mkReg(False);
Fifo#(ExecRedirect) redirect <- mkBypassFifo;
Fifo#(DecRedirect) decRedirect <- mkBypassFifo;
NextAddrPred#(16) nap <- mkBTB;
DirPred#(1024) dirPred <- mkBHT;
Notes: 19

## Slide 20: 4-Stage-BP pipeline Fetch rule: multiple predictors
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty)
begin redirect.deq; nap.update(redirect.first); end
if(redirect.notEmpty && redirect.first.mispredict)
begin pc <= redirect.first.nextPc; feEp <= !feEp; end
else if(decRedirect.notEmpty) begin
if(decRedirect.first.eEp == feEp) begin
fdEp <= !fdEp; pc <= decRedirect.first.nextPc; end
decRedirect.deq; end;
else begin
let ppc = nap.predPc(pc);
f2d.enq(Fetch2Decoode{pc: pc, ppc: ppc, inst: inst,
eEp: feEp, dEp: fdEp}); end
endrule
Not enough information is being passed from Fetch to Decode to train BHT – lab problem

## Slide 21: 4-Stage-BP pipeline Decode&RegRead Action
function Action decAndRegFetch(DInst dInst, Addr pc, Addr ppc,
Bool eEp);
action let stall = sb.search1(dInst.src1)|| sb.search2(dInst.src2);
if(!stall)
begin let rVal1 = rf.rd1(validRegValue(dInst.src1)); let rVal2 = rf.rd2(validRegValue(dInst.src2)); d2e.enq(Decode2Execute{pc: pc, ppc: ppc,
dInst: dInst, epoch: eEp,
rVal1: rVal1, rVal2: rVal2});
sb.insert(dInst.rDst);
end
endaction
endfunction

## Slide 22: 4-Stage-BP pipeline Decode&RegRead rule
rule doDecode;
let x = f2d.first; let inst = x.inst; let pc = x.pc;
let ppc = x.ppc; let idEp = x.dEp; let ieEp = x.eEp;
let dInst = decode(inst);
let nextPc = dirPrec.predAddr(pc, dInst);
if(ieEp != deEp) begin // change Decode’s epochs and
// continue normal instruction execution
deEp <= ieEp; let newdEp = idEp;
decAndRegRead(inst, pc, nextPc, ieEp);
if(ppc != nextPc) begin newdEp = !newdEp;
decRedirect.enq(DecRedirect{pc: pc,
nextPc: nextPc, eEp: ieEp}); end
dEp <= newdEp end
else if(idEp == dEp) begin decAndRegRead(inst, pc, nextPc, ieEp);
if(ppc != nextPc) begin
dEp <= !dEp; decRedirect.enq(DecRedirect{pc: pc,
newPc: newPc, eEp: ieEp}); end
end // if idEp!=dEp then drop,ie, no action
f2d.deq; endrule
BHT update is missing– lab problem

## Slide 23: 4-Stage-BP pipeline Execute rule: predictor training
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); e2c.enq(Exec2Commit{dst:eInst.dst, data:eInst.data}); if(eInst.mispredict) eEpoch <= !eEpoch
if(eInst.iType == J || eInst.iType == Jr || eInst.iType == Br) redirect.enq(Redirect{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken, mispredict: eInst.mispredict,
brType: eInst.iType}); end
else e2c.enq(Exec2Commit{dst:Invalid, data:?}); d2e.deq; endrule

## Slide 24: 4-Stage-BP pipeline Commit rule
rule doCommit;
let dst = eInst.first.dst;
let data = eInst.first.data;
if(isValid(dst))
rf.wr(tuple2(validValue(dst), data);
e2c.deq;
sb.remove;
endrule
Notes: 24

## Slide 25: Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor and the predictor uses this information to predict the resolution of the next branch
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition is false then so is second condition

## Slide 26: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Taken/¬Taken?
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Four
2k, 2-bit
Entry
BHT

## Slide 27: Uses of Jump Register (JR)
Switch statements (jump to address of matching case)
Dynamic function call (jump to run-time function address)
Subroutine returns (jump to return address)
How well does BTB or BHT work for each of these cases?
BTB works well if the same case is used repeatedly
BTB works well if the same function is usually called, (e.g., in C++ programming, when objects have same type in virtual function call)
BTB works well if return is usually to the same place
However, often one function is called from many distinct call sites!

## Slide 28: Subroutine Return Stack
A small structure to accelerate JR for subroutine returns is typically much more accurate than BTBs
pc of fb call
pc of fc call
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
pc of fd call
k entries
(typically k=8-16)
Pop return address when subroutine return decoded
Push call address when function call executed

## Slide 29: Multiple Predictors: BTB + BHT + Ret Predictors
One of the PowerPCs has all the three predictors
Performance analysis is quite difficult – depends upon the sizes of various tables and program behavior
Correctness: The system must work even if every prediction is wrong
Need
next PC immediately
Instr type, PC relative targets available
Simple conditions, register targets available
Complex conditions available
Next Addr
Pred
tight
loop
P C
Decode
Reg Read
Execute
Write
Back
mispred insts must be filtered
Br Dir Pred
Ret Addr stack JR
correct mispred