## Slide 1
Constructive Computer Architecture
Realistic Memories and Caches
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Multistage Pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
d2e
redirect
fEpoch
eEpoch
nap
e2c
scoreboard
The use of magic memories (combinational reads) makes such design unrealistic
Notes: 3

## Slide 4: Magic Memory Model
Reads and writes are always completed in one cycle
  a Read can be done any time (i.e. combinational)
  If enabled, a Write is performed at the rising clock edge
  (the write address and data must be stable at the clock edge)
MAGIC
RAM
ReadData
WriteData
Address
WriteEnable
Clock
In a real DRAM the data will be available several cycles after the address is supplied

## Slide 5: Memory Hierarchy
size: RegFile << SRAM << DRAM
latency: RegFile << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  hit (data Î fast memory)  low latency access
  miss (data Ï fast memory)  long latency access (DRAM)
Small,
Fast Memory
SRAM
CPU
RegFile
Big, Slow Memory
DRAM
holds frequently used data
why?
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 6: Inside a Cache
Cache
Processor
Main
Memory
Address
Address
Data
Data
copy of main mem
locations 100, 101, ...
Data Block
Line =
<Add tag, Data blk>
Data
Byte
Data
Byte
Data
Byte
100
304
6848
416
How many bits are needed for the tag?
Enough to uniquely identify the block
Address
Tag
Notes: Tag only needs enough bits to uniquely identify the block (jse)

## Slide 7: Cache Read
Search cache tags to find match for the processor generated address
Found in cache
a.k.a. hit
Return copy of data from cache
Not in cache
a.k.a. miss
Read block of data from Main Memory – may require writing back a cache line
Wait …
Return data to processor and update cache
Which line do we replace?

## Slide 8: Write behavior
On a write hit
  Write-through: write to both cache and the next level memory
  write-back: write only to cache and update the next level memory when line is evacuated
On a write miss
  Allocate – because of multi-word lines we first fetch the line, and then update a word in it
  Not allocate – word modified in memory
Notes: Write through vs. write back
WT:
+read miss never results in writes to main memory + main memory always has the most current copy of the data (consistent) - write is slower - every write needs a main memory access - as a result uses more memory bandwidth
WB:
+ writes occur at the speed of the cache memory + multiple writes within a block require only one write to main memory + as a result uses less memory bandwidth - main memory is not always consistent with cache - reads that result in replacement may cause writes of dirty blocks to main memory
Write Back with No Write Allocate: on hits it writes to cache setting dirty bit for the block, main memory is not updated; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the same block, if the block originally caused a miss, will generate misses all the way and result in very inefficient execution.
Hence, WB+WA more common combination.
Write Through with No Write Allocate: on hits it writes to cache and main memory; on misses it updates the block in main memory not bringing that block to the cache; Subsequent writes to the block will update main memory anyway, so write misses aren’t helped. Only read misses helped with allocate.
Hence, WT, no WA usually.
Re-look at these options when the next level is a cache; not a memory.
Write back with no allocate? Why is this

## Slide 9: Cache Line Size
A cache line usually holds more than one word
  Reduces the number of tags and the tag size needed to identify memory locations
  Spatial locality: Experience shows that if address x is referenced then addresses x+1, x+2 etc. are very likely to be referenced in a short time window
    consider instruction streams, array and record accesses
  Communication systems (e.g., bus) are often more efficient in transporting larger data sets

## Slide 10: Types of misses
Compulsory misses (cold start)
  First time data is referenced
  Run billions of instructions, become insignificant
Capacity misses
  Working set is larger than cache size
  Solution: increase cache size
Conflict misses
  Usually multiple memory locations are mapped to the same cache location to simplify implementations
  Thus it is possible that the designated cache location is full while there are empty locations in the cache.
  Solution: Set-Associative Caches
Notes: Compulsory: Prefetching, nothing much u can do
Capacity: Increase size, nothing much u can do
Conflict: Better cache design – set associative caches

## Slide 11: Internal Cache Organization
Cache designs restrict where in cache a particular address can reside
  Direct mapped: An address can reside in exactly one location in the cache. The cache location is typically determined by the lowest order address bits
  n-way Set associative: An address can reside in any of the a set of n locations in the cache. The set is typically determine by the lowest order address bits

## Slide 12: Direct-Mapped Cache
Tag
Data Block
V
=
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Block number
Block offset
What is a bad reference pattern?
Strided = size of cache
req address
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)

## Slide 13: Direct Map Address Selection higher-order vs. lower-order address bits
Tag
Data Block
V
=
Offset
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Tag
Why higher-order bits as tag may be undesirable?
Spatially local blocks conflict
Notes: Index and tag reversed
Why might this be undesirable? Spatially local blocks conflict.

## Slide 14: Reduce Conflict Misses
Memory time = Hit time + Prob(miss) * Miss penalty
Associativity: Reduce conflict misses by allowing blocks to go to several sets in cache
  2-way set associative: each block can be mapped to one of 2 cache sets
  Fully associative: each block can be mapped to any cache frame

## Slide 15: 2-Way Set-Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
hit
Tag
Data Block
V
Data
Word
or Byte
=
t
Notes: Compare latency to direct mapped case? (jse)

## Slide 16: Replacement Policy
In order to bring in a new cache line, usually another cache line has to be thrown out. Which one?
  No choice in replacement if the cache is direct mapped
Replacement policy for set-associative caches
  One that is not dirty, i.e., has not been modified
    In I-cache all lines are clean
    In D-cache if a dirty line has to be thrown out then it must be written back first
  Least recently used?
  Most recently used?
  Random?
How much is performance affected by the choice?
Difficult to know without benchmarks and quantitative measurements

## Slide 17: Blocking vs. Non-Blocking cache
Blocking cache:
  At most one outstanding miss
  Cache must wait for memory to respond
  Cache does not accept requests in the meantime
Non-blocking cache:
  Multiple outstanding misses
  Cache can continue to process requests while waiting for memory to respond to misses
We will first design a write-back, No write-miss allocate, blocking cache

## Slide 18: Blocking Cache Interface
interface Cache; method Action req(MemReq r);
method ActionValue#(Data) resp;
method ActionValue#(MemReq) memReq;
method Action memResp(Line r);
endinterface
cache
req
resp
memReq
memResp
Processor
DRAM or next level cache
hitQ
mReqQ
mRespQ
missReq
status

## Slide 19: Interface dynamics
The cache either gets a hit and responds immediately, or it gets a miss, in which case it takes several steps to process the miss
Reading the response dequeues it
Requests and responses follow the FIFO order
Methods are guarded, e.g., the cache may not be ready to accept a request because it is processing a miss
A status register keeps track of the state of the cache while it is processing a miss
typedef enum {Ready, StartMiss, SendFillReq, WaitFillResp} CacheStatus deriving (Bits, Eq);

## Slide 20: Blocking Cache code structure
module mkCache(Cache); RegFile#(CacheIndex, Line) dataArray <-
mkRegFileFull; … rule startMiss … endrule;
method Action req(MemReq r) … endmethod; method ActionValue#(Data) resp … endmethod; method ActionValue#(MemReq) memReq … endmethod; method Action memResp(Line r) … endmethod; endmodule
Internal communications is in line sizes but the processor interface, e.g., the response from the hitQ is word size

## Slide 21: Blocking cache state elements
RegFile#(CacheIndex, Line) dataArray <- mkRegFileFull;
RegFile#(CacheIndex, Maybe#(CacheTag))
tagArray <- mkRegFileFull;
RegFile#(CacheIndex, Bool) dirtyArray <- mkRegFileFull;
Fifo#(1, Data) hitQ <- mkBypassFifo;
Reg#(MemReq) missReq <- mkRegU;
Reg#(CacheStatus) status <- mkReg(Ready);
Fifo#(2, MemReq) memReqQ <- mkCFFifo;
Fifo#(2, Line) memRespQ <- mkCFFifo;
function CacheIndex getIdx(Addr addr) = truncate(addr>>2);
function CacheTag getTag(Addr addr) = truncateLSB(addr);
CF Fifos are preferable because they provide better decoupling. An extra cycle here may not affect the performance by much
Tag and valid bits are kept together as a Maybe type

## Slide 22: Req method hit processing
method Action req(MemReq r) if(status == Ready);
let idx = getIdx(r.addr); let tag = getTag(r.addr);
let currTag = tagArray.sub(idx);
let hit = isValid(currTag)?
fromMaybe(?,currTag)==tag : False;
if(r.op == Ld) begin
if(hit) hitQ.enq(dataArray.sub(idx));
else begin missReq <= r; status <= StartMiss; end
end
else begin // It is a store request
if(hit) begin dataArray.upd(idx, r.data);
dirtyArray.upd(idx, True); end
else memReqQ.enq(r); // write-miss no allocate
end
endmethod
It is straightforward to extend the cache interface to include a cacheline flush command
In case of multiword cache line, we only overwrite the appropriate word of the line

## Slide 23: Rest of the methods
method ActionValue#(Data) resp;
hitQ.deq;
return hitQ.first;
endmethod
method ActionValue#(MemReq) memReq;
memReqQ.deq;
return memReqQ.first;
endmethod
method Action memResp(Line r);
memRespQ.enq(r);
endmethod
Memory side methods

## Slide 24: Start miss rule
rule startMiss(status == StartMiss);
let idx = getIdx(missReq.addr);
let tag = tagArray.sub(idx);
let dirty = dirtyArray.sub(idx);
if(isValid(tag) && dirty) begin // write-back
let addr = {fromMaybe(?,tag), idx, 2'b0};
let data = dataArray.sub(idx);
memReqQ.enq(MemReq{op: St, addr: addr, data: data});
end
status <= SendFillReq;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready

## Slide 25: Send-fill and Wait-fill rules
rule sendFillReq (status == SendFillReq);
memReqQ.enq(missReq); status <= WaitFillResp;
endrule
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
Ready -> StartMiss -> SendFillReq -> WaitFillResp -> Ready
rule waitFillResp(status == WaitFillResp);
let idx = getIdx(missReq.addr);
let tag = getTag(missReq.addr);
let data = memRespQ.first;
dataArray.upd(idx, data);
tagArray.upd(idx, Valid (tag));
dirtyArray.upd(idx, False);
hitQ.enq(data); memRespQ.deq;
status <= Ready;
endrule
Notes: Is there a problem with waitFill? What if the hitQ is blocked? Should we not at least write it in the cache?

## Slide 26: Hit and miss performance
Hit
  Combinational read/write, i.e. 0-cycle response
  Requires req and resp methods to be concurrently schedulable, which in turn requires
  hitQ.enq < {hitQ.deq, hitQ.first}
  i.e., hitQ should be a bypass Fifo
Miss
  No evacuation: memory load latency plus combinational read/write
  Evacuation: memory store followed by memory load latency plus combinational read/write
Adding an extra cycle here and there in the miss case should not have a big negative performance impact

## Slide 27: Four-Stage Pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
f2d
Epoch
m2w
d2e
Next
Addr
Pred
scoreboard
insert bypass FIFO’s to deal with (0,n) cycle memory response
f12f2
e2m
Notes: 27

## Slide 28: now some coding ...
Integrating caches in to the 4-stage pipeline (F, D&R, E&M, W) from the last lecture
  Direction predictor training is incompletely specified
In L13 we discussed splitting a pipeline stage into two stages by inserting a bypass FIFO. We show it again here

## Slide 29: 4-Stage pipeline with BTB+BHT without caches
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU;
RFile rf <- mkBypassRFile;
IMemory iMem <- mkIMemory;
DMemory dMem <- mkDMemory;
Fifo#(1, Decode2Execute) d2e <- mkPipelineFifo;
Fifo#(1, Exec2Commit) e2c <- mkPipelineFifo;
Scoreboard#(2) sb <- mkPipelineScoreboard;
Reg#(Bool) feEp <- mkReg(False);
Reg#(Bool) fdEp <- mkReg(False);
Reg#(Bool) dEp <- mkReg(False);
Reg#(Bool) deEp <- mkReg(False);
Reg#(Bool) eEp <- mkReg(False);
Fifo#(ExecRedirect) redirect <- mkBypassFifo;
Fifo#(DecRedirect) decRedirect <- mkBypassFifo;
NextAddrPred#(16) nap <- mkBTB;
DirPred#(1024) dirPred <- mkBHT;
Notes: 29

## Slide 30: 4-Stage pipeline with BTB+BHT with caches
module mkProc(Proc);
Reg#(Addr) pc <- mkRegU; Rfile rf <- mkBypassRFile;
Cache#(ICacheSize) iCache <- mkCache;
Cache#(DCacheSize) dCache <- mkCache;
Fifo#(1, Fetch2Decode) f12f2 <- mkBypassFifo;
Fifo#(1, Maybe#{Einst}) e2m <- mkBypassFifo;
Fifo#(1, Decode2Execute) d2e <- mkPipelineFifo;
Fifo#(1, Exec2Commit) m2w <- mkPipelineFifo;
Scoreboard#(2) sb <- mkPipelineScoreboard;
Reg#(Bool) feEp <- mkReg(False);
Reg#(Bool) fdEp <- mkReg(False);
Reg#(Bool) dEp <- mkReg(False);
Reg#(Bool) deEp <- mkReg(False);
Reg#(Bool) eEp <- mkReg(False);
Fifo#(ExecRedirect) execRedirect <- mkBypassFifo;
Fifo#(DecRedirect) decRedirect <- mkBypassFifo;
AddrPred#(16) addrPred <- mkBTB;
DirPred#(1024) dirPred <- mkBHT;
Notes: 30

## Slide 31: 4-Stage pipeline with BTB+BHT without caches
rule doFetch; let inst = iMem.req(pc); if(redirect.notEmpty)
begin redirect.deq; nap.update(redirect.first); end
if(redirect.notEmpty && redirect.first.mispredict)
begin pc <= redirect.first.nextPc; feEp <= !feEp; end
else if(decRedirect.notEmpty) begin
if(decRedirect.first.eEp == feEp) begin
fdEp <= !fdEp; pc <= decRedirect.first.nextPc; end
decRedirect.deq; end;
else begin
let ppc = nap.predPc(pc);
f2d.enq(Fetch2Decoode{pc: pc, ppc: ppc, inst: inst,
eEp: feEp, dEp: fdEp}); end
endrule
make a iMem request and enqueue into f12f2
where?

## Slide 32: 4-Stage pipeline with BTB+BHT with caches
rule doFetch1; if(redirect.notEmpty)
begin redirect.deq; nap.update(redirect.first); end
if(redirect.notEmpty && redirect.first.mispredict)
begin pc <= redirect.first.nextPc; feEp <= !feEp; end
else if(decRedirect.notEmpty) begin
if(decRedirect.first.eEp == feEp) begin
fdEp <= !fdEp; pc <= decRedirect.first.nextPc; end
decRedirect.deq; end;
else begin
let ppc = nap.predPc(pc);
iCache.req(MemReq{op: Ld, addr: pc, data:?}); f12f2.enq(Fetch2Decoode{pc: pc, ppc: ppc, inst: ?,
eEp: feEp, dEp: fdEp});
end
endrule
PC
iMem
f2d
Epoch
nap
f12f2

## Slide 33: 4-Stage pipeline Fetch2 rule
rule doFetch2;
let inst <- iCache.resp;
let f2dVal = f12f2.first;
f2dVal.inst = inst;
f12f2.deq;
f2d.enq(f2dVal);
endrule
PC
iMem
f2d
Epoch
nap
f12f2
Execute rule can be split in two rules in a similar manner to deal with dCache
next store buffers and non-blocking caches

## Slide 34: 4-Stage pipeline Execute rule
rule doExecute; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dMem.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dMem.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); e2c.enq(Exec2Commit{dst:eInst.dst, data:eInst.data}); if(eInst.mispredict) eEpoch <= !eEpoch
if(eInst.iType == J || eInst.iType == Jr || eInst.iType == Br) redirect.enq(Redirect{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken, mispredict: eInst.mispredict,
brType: eInst.iType}); end
else e2c.enq(Exec2Commit{dst:Invalid, data:?}); d2e.deq; endrule

## Slide 35: 4-Stage pipeline Execute rule with caches
rule doExecute1; let x = d2e.first;
let dInst = x.dInst; let pc = x.pc;
let ppc = x.ppc; let epoch = x.epoch;
let rVal1 = x.rVal1; let rVal2 = x.rVal2;
if(epoch == eEpoch) begin
let eInst = exec(dInst, rVal1, rVal2, pc, ppc); if(eInst.iType == Ld) eInst.data <-
dCache.req(MemReq{op:Ld, addr:eInst.addr, data:?}); else if (eInst.iType == St) let d <-
dCache.req(MemReq{op:St, addr:eInst.addr, data:eInst.data}); e2m.enq(Valid (eInst)); if(eInst.mispredict) eEpoch <= !eEpoch
if(eInst.iType == J || eInst.iType == Jr || eInst.iType == Br) redirect.enq(Redirect{pc: pc, nextPc: eInst.addr,
taken: eInst.brTaken, mispredict: eInst.mispredict,
brType: eInst.iType}); end
else e2m.enq(Invalid); d2e.deq; endrule

## Slide 36: 4-Stage pipeline Execute2 rule
rule doExecute2;
let eInst = e2m.first;
if(isValid(eInst)) begin
let x = validValue(eInst);
if(x.iType == Ld)
x.data <- dCache.resp;
m2w.enq(Exec2Commit{dst:x.dst, data:x.data});
end
else
m2w.enq(Exec2Commit{dst:Invalid, data:?});
e2m.deq; endrule