## Slide 1
Constructive Computer Architecture
Store Buffers and
Non-blocking Caches
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Non-blocking cache
Completion buffer controls the entries of requests and ensures that departures take place in order even if loads complete out-of-order
requests to the backend have to be tagged
cache
req
resp
mReq
mResp
mReqQ
mRespQ
req proc
FIFO
responses
OOO
responses
Processor
req
resp
cbuf

## Slide 4: Completion buffer: Interface
cbuf
interface CBuffer#(type t);
method ActionValue#(Token) getToken;
method Action put(Token tok, t d);
method ActionValue#(t) getResult;
endinterface
getResult
getToken
put (result & token)
Concurrency requirement
getToken < put < getResult

## Slide 5: Non-blocking FIFO Cache
module mkNBFifoCache(Cache); CBuffer cBuf <- mkCompletionBuffer;
NBCache nbCache <- mkNBtaggedCache;
rule nbCacheResponse;
let x <- nbCache.resp;
cBuf.put(x);
endrule method Action req(MemReq x); let tok <- cBuf.getToken;
nbCache.req(TaggedMemReq{req:x, tag:tok});
endmethod
method MemResp resp; let x <- cBuf.getResult
return x endmethod
endmodule
req
resp
cbuf

## Slide 6: Non-blocking Cache
St
Q
Ld
Buff
Wait
Q
V/
D/
I/
W
Tag
Data
wbQ
mReqQ
mRespQ
hitQ
resp
req
1
2
3
Waiting load reqs after the req for data has been made
An extra bit in the cache to indicate if the data for a line is present
Holds St reqs that have not been sent to cache/ memory
load reqs before the req for data has been made
Behavior to be described by 4 concurrent FSMs
St req goes in StQ; Ld req searches:
StQ
Cache
LdQ
Notes: 6

## Slide 7: Incoming req
Type of request
Put in stQ
In stQ?
bypass hit
in cache?
with data?
in ldBuf?
hit
put in waitQ
(data on the way from mem)
put in waitQ
put in ldBuf
& waitQ
st
ld
yes
no
yes
no
yes
no
yes
no

## Slide 8: Store buffer processing the oldest entry
Tag in cache?
Data in data?
update
cache
wbReq
(no-allocate-on-write-miss policy
wait
yes
no
yes
no

## Slide 9: Load buffer processing the oldest entry
Evacuation needed?
Wb Req
replace tag
data missing
fill Req
replace tag
data missing
fill Req
yes
no

## Slide 10: Mem Resp (line)
Update cache
Process all req in waitQ for the addresses in the line

## Slide 11: Completion buffer: Implementation
I
I
V
I
V
I
cnt
iidx
ridx
buf
A circular buffer with two pointers iidx and ridx, and a counter cnt
Elements are of Maybe type
module mkCompletionBuffer(CompletionBuffer#(size));
Vector#(size, EHR#(Maybe#(t))) cb
<- replicateM(mkEHR(Invalid));
Reg#(Bit#(TAdd#(TLog#(size),1))) iidx <- mkReg(0);
Reg#(Bit#(TAdd#(TLog#(size),1))) ridx <- mkReg(0);
EHR#(Bit#(TAdd#(TLog#(size),1))) cnt <- mkEHR(0);
Integer vsize = valueOf(size);
Bit#(TAdd#(TLog#(size),1)) sz = fromInteger(vsize);
rules and methods...
endmodule

## Slide 12: Completion Buffer cont
method ActionValue#(t) getToken() if(cnt.r0!==sz);
cb[iidx].w0(Invalid);
iidx <= iidx==sz-1 ? 0 : iidx + 1;
cnt.w0(cnt.r0 + 1);
return iidx;
endmethod
method Action put(Token idx, t data);
cb[idx].w1(Valid data);
endmethod
method ActionValue#(t) getResult() if(cnt.r1 !== 0
&&&(cb[ridx].r2 matches tagged (Valid .x));
cb[ridx].w2(Invalid);
ridx <= ridx==sz-1 ? 0 : ridx + 1;
cnt.w1(cnt.r1 – 1);
return x;
endmethod
getToken < put < getResult
Notes: 12