## Slide 1
Constructive Computer Architecture
Interrupts/Exceptions/Faults
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Interrupts altering the normal flow of control
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.
program
HI1
HI2
HIn
interrupt
handler
Ii-1
Ii
Ii+1

## Slide 4: Causes of Interrupts events that request the attention of the processor
Asynchronous: an external event
  input/output device service-request/response
  timer expiration
  power disruptions, hardware failure
Synchronous: an internal event (a.k.a exceptions, faults and traps)
  undefined opcode, privileged instruction
  arithmetic overflow, FPU exception
  misaligned memory access
  virtual memory exceptions: page faults, TLB misses, protection violations
  traps: system calls, e.g., jumps into kernel

## Slide 5: Asynchronous Interrupts: invoking the interrupt handler
An I/O device requests attention by asserting one of the prioritized interrupt request lines
After the processor decides to process the interrupt
  It stops the current program at instruction Ii, completing all the instructions up to Ii-1 (Precise interrupt)
  It saves the PC of instruction Ii in a special register (EPC)
  It disables interrupts and transfers control to a designated interrupt handler running in the kernel mode
    Privileged/user mode to prevent user programs from causing harm to other users or OS
Usually speed is not the paramount concern in handling interrupts

## Slide 6: Interrupt Handler
Saves EPC before enabling interrupts to allow nested interrupts 
  need an instruction to move EPC into GPRs
  need a way to mask further interrupts at least until EPC can be saved
Needs to read a status register that indicates the cause of the interrupt
Uses a special indirect jump instruction ERET (return-from-exception) which
  enables interrupts
  restores the processor to the user mode
  restores hardware status and control state

## Slide 7: Synchronous Interrupts
A synchronous interrupt is caused by a particular instruction and causes a control hazard
  requires undoing the effect of one or more partially executed instructions. Comes in two varieties:
Exception: The instruction cannot be completed and needs to be restarted after the exception has been handled
  information about the exception has to be recorded and conveyed to the exception handler
Faults (aka Trap): Like a system call and the instruction is considered to have been completed
  requires a special jump instruction involving a change to privileged kernel mode

## Slide 8: Synchronous Interrupt Handling
Overflow
Illegal Opcode
PC address Exception
Data address Exceptions
...
PC
Inst. Mem
Decode
Data Mem
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
WB
When an instruction causes multiple exceptions the first one has to be processed

## Slide 9: Additional Features for Exceptions/Faults
register: epc
  holds pc+4 of instruction that causes exception/fault
instruction: eret
  returns from an exception/fault handler sub-routine using epc
As an example consider a complex instruction which may be implemented in SW
mult ra, rb
  causes a fault, sets epc to pc+4
  jumps to the exception handler for mult
  the mult instruction is considered to have been completed
Notes: 9

## Slide 10
Software Considerations
00001004 <handler>:
1004: 00000000 li $t1, 1010
// all exceptions jump to 1004
1008: 00000000 addiu $t1, causeR
// causeR contains 0 for mul, 4 for div, etc
100c: 00000000 jr $t1
1010: 08000408 j 1020 // <mult_excep>
1014: 08000408 j 1060 // <div_excep>
...
00001020 <mult_excep>:
1020: 24890000 addiu $t1,$a0,0
1024: 24aa0000 addiu $t2,$a1,0
...
104c: 42000018 eret
...
00001124 <main>:
...
11a0: 00850018 mult $a0,$a1
Notes: 10

## Slide 11: We need to change the interfaces to handle exceptions wherever necessary
For example,
a memory request will return a
2-tuple <mem-reponse, mException>;
- decoder will have to recognize new instructions mult, eret, ...

## Slide 12: Decoded Instruction
typedef struct {
IType iType;
AluFunc aluFunc;
BrFunc brFunc;
Maybe#(FullIndx) dst;
Maybe#(FullIndx) src1;
Maybe#(FullIndx) src2;
Maybe#(Data) imm;
} DecodedInst deriving(Bits, Eq);
typedef enum {Unsupported, Alu, Ld, St, J, Jr, Br, Mult, ERet} IType deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu, LShift, RShift, Sra} AluFunc deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT} BrFunc deriving(Bits, Eq);
Bit#(6) fcMULT = 6'b011000;
Bit#(5) rsERET = 5'b10000;

## Slide 13: Decode
function DecodedInst decode(Data Inst);
DecodedInst dInst = ?; ...
opFUNC: begin
case (funct) ...
fcMULT:
dInst.iType = Mult;
dInst.brFunc = AT;
dInst.rDst = Invalid;
dInst.rSrc1 = validReg(rs);
dInst.rSrc2 = validReg(rt); end
opRS: begin
if(rs==rsERET)
dInst.iType = ERet;
dInst.brFunc = AT;
dInst.rDst = Invalid;
dInst.rSrc1 = Invalid;
dInst.rSrc2 = Invalid; end
return dInst;
endfunction
Notes: 13

## Slide 14: Branch Address Calculation
function Addr brAddrCalc(Addr pc, Data val,
IType iType, Data imm, Bool taken, Addr epc);
Addr pcPlus4 = pc + 4;
Addr targetAddr = case (iType)
J : {pcPlus4[31:28], imm[27:0]};
Jr : val;
Br : (taken? pcPlus4 + imm : pcPlus4);
Mult: h’1004; // Interrupt handler
ERet: epc;
Alu, Ld, St, Unsupported: pcPlus4;
endcase;
return targetAddr;
endfunction
Notes: 14

## Slide 15: Execute Function
function ExecInst exec(DecodedInst dInst, Data rVal1,
Data rVal2, Addr pc, Addr epc);
...
let brAddr = brAddrCalc(pc, rVal1, dInst.iType,
validValue(dInst.imm), brTaken, epc); ...
eInst.brAddr = ... brAddr ...;
...
return eInst;
endfunction
With these changes the single-cycle machine will handle exceptions

## Slide 16: One-Cycle SMIPS
rule doExecute;
let inst = iMem.req(pc); let dInst = decode(inst);
let rVal1 = rf.rd1(validRegValue(dInst.src1));
let rVal2 = rf.rd2(validRegValue(dInst.src2));
let eInst = exec(dInst, rVal1, rVal2, pc, epc);
if(eInst.iType == Ld)
eInst.data <- dMem.req(MemReq{op: Ld, addr:
eInst.addr, data: ?});
else if(eInst.iType == St)
let d <- dMem.req(MemReq{op: St, addr:
eInst.addr, data: eInst.data});
if (isValid(eInst.dst))
rf.wr(validRegValue(eInst.dst), eInst.data);
pc <= eInst.brTaken ? eInst.addr : pc + 4;
if(eInst.iType == Mult) begin
epc <= eInst.addr; causeR <= 0; end
endrule endmodule
Notes: 16

## Slide 17: Exception handling in pipeline machines

## Slide 18: Exception Handling
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Ex
D
PC
D
Ex
E
PC
E
Ex
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point
1. An instruction may cause multiple exceptions; which one should we process?
2. When multiple instructions are causing exceptions; which one should we process first?
from the earliest stage
from the oldest instruction

## Slide 19: Exception Handling
When instruction x in stagei raises an exception, its cause is recorded and passed down the pipeline
For a given instruction, exceptions from the later stages of the pipeline do not override cause of exception from the earlier stages
At commit point external interrupts, if present, override other internal interrupts
If an exception is present at commit: Cause and EPC registers are set, and pc is redirected to the handler PC
  Epoch mechanism takes care of redirecting the pc

## Slide 20: Multiple stage pipeline
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
f2d
Epoch
m2c
d2e
Next
Addr
Pred
scoreboard
f12f2
e2m
wrong path insts are dropped
wrong path insts are poisoned
This affects whether an instruction is removed from sb in case of an interrupt
external interrupts considered at Commit
Notes: 20

## Slide 21: Interrupt processing
Internal interrupts can happen at any stage but cause a redirection only at Commit
External interrupts are considered only at Commit
Some instructions, like Store, cannot be undone once launched. So an instruction is considered to have completed before an external interrupt is taken
If an instruction causes an interrupt then the external interrupt, if present, is given a priority and the instruction is executed again

## Slide 22: Interrupt processing at Execute-1
Incoming Interrupt cause
-if (mem type) issue Ld/St
-if (mispred) redirect
-pass eInst to M stage
-pass eInst to M stage unmodified
none
! none
eInst will contain information about any newly detected interrupts at Execute

## Slide 23: Interrupt processing at Execute-2 or Mem stage
Incoming Interrupt cause
-pass eInst with modified data to Commit
-pass eInst to Commit unmodified
none
! none
Memory Interrupt?
no
yes
-pass new Cause to Commit

## Slide 24: Interrupt processing at Commit
External Interrupt?
EPC<= if (Exception) pc : pc+4;
causeR <= inCause;
if (inCause after Reg Fetch) sb.rm;
mode <= Privlage;
Redirect
no
yes
Incoming cause
none
! none
none
! none
-commit
-sb.rm
Incoming cause
commit;
sb.rm;
EPC<= ppc;
causeR <= Ext;
mode <= Privlage;
Redirect
EPC<= pc;
causeR <= Ext;
if (inCause after Reg Fetch) sb.rm;
mode <= Privlage;
Redirect