## Slide 1
Constructive Computer Architecture
Virtual Memory:
From Address Translation to Demand Paging
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  Each user has one private and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price of VM is address translation on each memory reference
OS
useri
VA
PA
mapping
TLB
Swapping Store
Primary
Memory

## Slide 4: Names for Memory Locations
Machine language address
  as specified in machine code
Virtual address
  ISA specifies translation of machine code address into virtual address of program variable (sometime called effective address)
Physical address
  operating system specifies mapping of virtual address into name for a physical memory location
physical
address
virtual
address
machine
language
address
Address
Mapping
ISA
Physical Memory
(DRAM)

## Slide 5: Paged Memory Systems
Processor generated address can be interpreted as a pair <page number, offset>
A page table contains the physical address of the base of each page
Page tables make it possible to store the pages of a program non-contiguously
0
1
2
3
Address Space
of User-1
Page Table
of User-1
0
1
2
3
1
0
2
3
page number offset
Notes: Relaxes the contiguous allocation requirement.

## Slide 6: Private Address Space per User
Each user has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical
Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 7: Page Tables in Physical Memory
VA1
User 1
PT User 1
PT User 2
VA1
User 2
Idea: cache the address translation of frequently used pages – Translation Look-aside Buffer (TLB)
Two memory references are required to access a virtual address.
100% overhead!

## Slide 8: Linear Page Table
VPN
Offset
Virtual address
PT Base Register
VPN
Data word
Data Pages
Offset
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN
Page Table Entry (PTE) contains:
  A bit to indicate if a page exists
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Status bits for protection and usage
OS sets the Page Table Base Register whenever active user process changes

## Slide 9: Size of Linear Page Table
With 32-bit addresses, 4-KB pages & 4-byte PTEs
  220 PTEs, i.e, 4 MB page table per user
  4 GB of swap space needed to back up the full virtual address space
Larger Pages can reduce the overhead but cause
  Internal fragmentation (Not all memory in a page is used)
  Larger page-fault penalty (more time to read from disk)
What about 64-bit virtual address space?
  Even 1MB pages would require 244 8-byte PTEs (35 TB!)
Any “saving grace” ?
Page tables are sparsely populated and hence hierarchical organization can help

## Slide 10: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the
Page Table
p1
offset
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index

## Slide 11: Address Translation & Protection
A good VM design needs to be fast and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write
Every instruction access and data access needs address translation and protection checks
Address translation is very expensive!
  In a one-level page table, each reference becomes two or more memory accesses

## Slide 12: Translation Lookaside Buffers (TLB)
Cache address translations in TLB
TLB hit  Single Cycle Translation
TLB miss  Page Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 13: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
Random or FIFO replacement policy
Process ID information in TLB?
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach =
64 entries * 4 KB = 256 KB

## Slide 14: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB
  A privileged “untranslated” addressing mode is used for PT walk
Hardware (SPARC v8, x86, PowerPC)
  A memory management unit (MMU) walks the page tables and reloads the TLB
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page-Fault exception for the original instruction

## Slide 15: Translation for Page Tables
Can references to page tables cause TLB misses?
User Page Table
(in virtual space)
User PTE Base
User VA translation causes a TLB miss
Page table walk: User PTE Base and appropriate bits from VA are used to obtain virtual address (VP) for the page table entry
Suppose we get a TLB miss when we try to translate VP?
Must know the physical address of the page table
Notes: Present the virtual address V to the TLB and there was a TLB miss. On a TLB miss, you have to perform a page table walk. Use the User PTE Base and the bits from the virtual address V corresponding to the first-level of the page table to find the page table entry in virtual space V_P. Search TLB for V_P. Get a second TLB miss. How to translate V_P? Add System PTE Base to bits from V_P to find physical address of page table entry for V_P. This addition corresponds to no-translation addressing mode.
You have to know where the system page table is in physical space.

## Slide 16: Translation for Page Tables continued
On a TLB miss during a VP translation, OS adds System PTE Base to bits from VP to find physical address of page table entry for the VP
A program that traverses the page table needs a “no translation” addressing mode
User Page Table
(in virtual space)
User PTE Base
System Page Table (in physical space)
System PTE Base
Notes: Present the virtual address V to the TLB and there was a TLB miss. On a TLB miss, you have to perform a page table walk. Use the User PTE Base and the bits from the virtual address V corresponding to the first-level of the page table to find the page table entry in virtual space V_P. Search TLB for V_P. Get a second TLB miss. How to translate V_P? Add System PTE Base to bits from V_P to find physical address of page table entry for V_P. This addition corresponds to no-translation addressing mode.
You have to know where the system page table is in physical space.

## Slide 17: Handling a Page Fault
When the referenced page is not in DRAM:
  The missing page is located (or created)
  It is brought in from disk, and page table is updated
    Another job may be run on the CPU while the first job waits for the requested page to be read from disk
  If no free pages are left, a page is swapped out
    approximate LRU replacement policy
Since it takes a long time (msecs) to transfer a page, page faults are handled completely in software (OS)
  Untranslated addressing mode is essential to allow kernel to access page tables

## Slide 18: Swapping a Page of a Page Table
A PTE in primary memory contains
primary or secondary memory addresses
A PTE in secondary memory contains
only secondary memory addresses
 a page of a PT can be swapped out only
if none its PTE’s point to pages in the
primary memory
Why?
Don’t want to cause a page fault during translation when the data is in memory
Notes: What is the worst thing you can do with respect to storing page tables?
Storing page table on disk for whose entries point to phys. Mem.

## Slide 19: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 20: Caching vs. Demand Paging
CPU
cache
primary
memory
secondary
memory
Caching Demand paging
  cache entry page frame
  cache block (~32 bytes) page (~4K bytes)
  cache miss rate (1% to 20%) page miss rate (<0.001%)
  cache hit (~1 cycle) page hit (~100 cycles)
  cache miss (~100 cycles) page miss (~5M cycles)
  a miss is handled a miss is handled
  in hardware mostly in software
primary
memory
CPU

## Slide 21: Address Translation in CPU Pipeline
Software handlers need a restartable exception on page fault or protection violation
Handling a TLB miss needs a hardware or software mechanism to refill TLB
Need mechanisms to cope with the additional latency of a TLB:
  slow down the clock
  pipeline the TLB and cache access
  virtual address caches
  parallel TLB/cache access
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

Notes: Restartable exception is going back to the same LD/ST instruction. If we have a divide by zero exception, we don’t go back to the instruction that caused the exception.

## Slide 22: Physical or Virtual Address Caches?
one-step process in case of a hit (+)
cache needs to be flushed on a context switch unless address space identifiers (ASIDs) included in tags (-)
aliasing problems due to the sharing of pages (-)
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
Alternative: place the cache before the TLB
CPU
VA
(StrongARM)
Virtual
Cache
PA
TLB
Primary
Memory

## Slide 23: Aliasing in Virtual-Address Caches
VA1
VA2
Page Table
Data Pages
PA
VA1
VA2
1st Copy of Data at PA
2nd Copy of Data at PA
Tag
Data
Two virtual pages share one physical page
Virtual cache can have two copies of same physical data. Writes to one copy not visible to reads of other!
General Solution: Disallow aliases to coexist in cache
Software (i.e., OS) solution for direct-mapped cache
  VAs of shared pages must agree in cache index bits; this ensures all VAs accessing same PA will conflict in direct-mapped cache (early SPARCs)
Notes: Two processes sharing the same file,
Map the same memory segment to different
Parts of their address space.

## Slide 24: Concurrent Access to TLB & Cache
Index L is available without consulting the TLB
  cache and TLB accesses can begin simultaneously
Tag comparison is made after both accesses are completed
Cases: L + b = k L + b < k
L + b > k what happens here?
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k
Partially VA cache!
Notes: Tag size = {PA} – L – b
What if you want to build a large cache where L + b > k?

## Slide 25: Virtual-Index Physical-Tag Caches: Associative Organization
VPN L = k-b b
TLB
Direct-map
2L blocks
PPN Page Offset
=
hit?
Data
Phy.
Tag
Tag
VA
PA
Virtual
Index
k
Direct-map
2L blocks
=
After the PPN is known, W physical tags are compared
Allows cache size to be greater than 2L+b bytes
W ways

## Slide 26: We change the cache interface minimally and assume that the Address translation is done as part of the memory system
A memory request will return a 2-tuple <mem-reponse, mException>
Coding is straightforward but we do not have adequate testing infrastructure: requires implementing at least rudimentary TLB-miss and page-fault handlers