## Slide 1
Constructive Computer Architecture
Cache Coherence
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Memory Consistency in SMPs
Suppose CPU-1 updates A to 200.
  write-back: memory and cache-2 have stale values
  write-through: cache-2 has a stale value
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100
200
200
Do these stale values matter?
What is the view of shared memory for programming?

## Slide 4: Maintaining Store Atomicity
Store atomicity requires all processors to see writes occur in the same order
  multiple copies of a location in various caches can cause this to be violated
To meet the ordering requirement it is sufficient for hardware to ensure:
  Only one processor at a time has write permission for a location
  No processor can load a stale copy of the data after a write to the location
       cache coherence protocols

## Slide 5: A System with Multiple Caches
M
L1
P
L1
P
L1
P
L1
P
L2
L2
L1
P
L1
P
Interconnect
Modern systems often have hierarchical caches
Each cache has exactly one parent but can have zero or more children
Logically only a parent and its children can communicate directly
Inclusion property is maintained between a parent and its children, i.e.,
a  Li  a  Li+1
Because usually
Li+1 >> Li

## Slide 6: Cache Coherence Protocols
Write request:
  the address is invalidated in all other caches before the write is performed, or
  the address is updated in all other caches after the write is performed
Read request:
  if a dirty copy is found in some cache, that is the value that must be used, e.g., by doing a write-back and reading the memory or forwarding that dirty value directly to the reader.
We will focus on Invalidation protocols as opposed to Update protocols

## Slide 7: State needed to maintain Cache Coherence
Use MSI encoding in caches where
  I means this cache does not contain the location
  S means this cache has the location but so may other caches; hence it can only be read
  M means only this cache has the location; hence it can be read and written
The states M, S, I can be thought of as an order M > S > I
  A transition from a lower state to a higher state is called an Upgrade
  A transition from a higher state to a lower state is called a Downgrade

## Slide 8: Sibling invariant and compatibility
Sibling invariant:
  Cache is in state M  its siblings are in state I
  That is, the sibling states are “compatible”
The states x, y of two siblings are compatible iff IsCompatible(x, y) is True where
    IsCompatible(M, M) = False
    IsCompatible(M, S) = False
    IsCompatible(S, M) = False
    All other cases = True

## Slide 9: Cache State Transitions
S
M
I
store
load
write-back
invalidate
flush
store
optimizations
This state diagram is helpful as long as one remembers that each transition involves cooperation of other caches and the main memory

## Slide 10: Cache Actions
On a read miss (i.e., Cache state is I):
  In case some other cache has the location in state M then write back the dirty data to Memory
  Read the value from Memory and set the state to S
On a write miss (i.e., Cache state is I or S):
  Invalidate the location in all other caches and in case some cache has the location in state M then write back the dirty data
  Read the value from Memory if necessary and set the state to M
Misses cause Cache upgrade actions which in turn may cause further downgrades or upgrades on other caches

## Slide 11: MSI protocol: some issues
It is possible to have multiple requests for the same location from different processors. Hence there is a need to arbitrate requests
  In bus-based systems bus controller performs this function
  In directory-based systems upgrade requests are passed to the parent who acts as an arbitrator
On a cache miss there is a need to find out the state of other caches
  In a bus-based system a system-wide broadcast of the request determines the state of other caches by “snooping”
  In directory-based systems a directory keeps track of the state of each child cache

## Slide 12: Directory State Encoding Two-level (L1, M) system
For each location in a cache, the directory keeps two types of info
  c.state[a] (sibling info): do c’s siblings have a copy of location a; M (means no), S (means maybe)
  c.child[ck][a] (children info): the state of c’s child ck for location a; At most one child can be in state M
Since L1 has no children, only sibling information is kept and since main (home) memory has no siblings only children cache information is kept
All addresses in the home memory are in state M
a
a
P
L1
P
L1
L1
Interconnect
<S,I,I,I>
S
P
P

## Slide 13: Directory state encoding cont
New states needed to deal with waiting for responses:
  c.waitp[a] : Denotes if cache c is waiting for a response from its parent
    Nothing means not waiting
    Valid (M|S|I) means waiting for a response to transition to M or S or I state, respectively
  c.waitc[ck][a] : Denotes if cache c is waiting for a response from its child ck
    Nothing | Valid (M|S|I)
Cache state in L1:
    <(M|S|I), (Nothing | Valid(M|S|I))>
Directory state in home memory:
  <[(M|S|I), (Nothing | Valid(M|S|I))]>
Children’s state

## Slide 14: A Directory-based Protocol an abstract view
interconnect
PP
P
c2m
m2c
L1
p2m
m2p
m
PP
in
out
PP
P
c2m
m2c
L1
p2m
m2p
Each cache has 2 pairs of queues
  (c2m, m2c) to communicate with the memory
  (p2m, m2p) to communicate with the processor
Message format: <cmd, srcdst, a, s, data>
FIFO message passing between each (srcdst) pair except a Resp cannot block a Req
Req/Resp
address
state

## Slide 15: Processor Hit Rules
Load-hit rule
  p2m.msg=(Load a) &
  (c.state[a]>I)
 p2m.deq;
m2p.enq(c.data[a]);
Store-hit rule
    p2m.msg=(Store a v) &
  c.state[a]=M
 p2m.deq;
m2p.enq(Ack);
c.data[a]:=v;
PP
P
c2m
m2c
L1
p2m
m2p
The miss rules are taken care of by the general cache rules to be presented

## Slide 16: Processing a Load or a Store miss
Child to Parent: Upgrade-to-y request
Parent to Child: process Upgrade-to-y request
Parent to other child caches: Downgrade-to-x request
Child to Parent: Downgrade-to-x response
Parent waits for all Downgrade-to-x responses
Parent to Child: Upgrade-to-y response
Child receives upgrade-to-y response

## Slide 17: Processing a Load miss
L1 to Parent: Upgrade-to-S request
  (c.state[a]=I) & (c.waitp[a]=Nothing)
   c.waitp[a]:=Valid S;
  c2m.enq(<Req, cm, a, S, - >);
Parent to L1: Upgrade-to-S response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,S,-> & (i≠c, IsCompatible(m.child[i][a],S))
   m2c.enq(<Resp, mc, a, S, m.data[a]>);
  m.child[c][a]:=S; c2m.deq
L1 receiving upgrade-to-S response
  m2c.msg=<Resp, mc, a, S, data>
   m2c.deq; c.data[a]:=data; c.state[a]:=S;
  c.waitp[a]:=Nothing;

## Slide 18: Processing Load miss cont.
What if (i≠c, IsCompatible(m.child[i][a],y)) is false?
Downgrade other child caches
Parent to L1: Upgrade-to-S response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,S,-> & (i≠c, IsCompatible(m.child[i][a],S))
   m2c.enq(<Resp, mc, a, S, m.data[a]>);
  m.child[c][a]:=S; c2m.deq
Parent to Child: Downgrade to S request
c2m.msg=<Req,cm,a,S,-> &
  (m.child[i][a]>S) & (m.waitc[i][a]=Nothing)
   m.waitc[i][a]:=Valid S; m2c.enq(<Req, mi, a, S, - >);

## Slide 19: Complete set of cache actions
req = {1,4,7}
resp = {2,3,5,6,8}
A protocol specifies cache actions corresponding to each of these 8 different messages
Cache
1,5,8
3,7
Memory
4,2
6

## Slide 20: Child Requests
1. Child to Parent: Upgrade-to-y Request
  (c.state[a]<y) & (c.waitp[a]=Nothing)
   c.waitp[a]:=Valid y;
  c2m.enq(<Req, cm, a, y, - >);

## Slide 21: Parent Responds
2. Parent to Child: Upgrade-to-y response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,y,-> & (m.child[c][a]<y) & (i≠c, IsCompatible(m.child[i][a],y))
   m2c.enq(<Resp, mc, a, y,
  (if (m.child[c][a]=I) then m.data[a] else -)>);
  m.child[c][a]:=y; c2m.deq;

## Slide 22: Child receives Response
3. Child receiving upgrade-to-y response
  m2c.msg=<Resp, mc, a, y, data>
   m2c.deq;
  if(c.state[a]=I) c.data[a]:=data;
  c.state[a]:=y;
  if(c.waitp[a]=(Valid x) & x≤y) c.waitp[a]:=Nothing;

## Slide 23: Parent Requests
4. Parent to Child: Downgrade-to-y Request
  (m.child[i][a]>y) & (m.waitc[i][a]=Nothing)
   m.waitc[i][a]:=Valid y;
  m2c.enq(<Req, mc, a, y, - >);

## Slide 24: Child Responds
5. Child to Parent: Downgrade-to-y response
  (m2c.msg=<Req,mc,a,y,->) & (c.state[a]>y)
   c2m.enq(<Resp, c->m, a, y,
  (if (c.state[a]=M) then c.data[a] else - )>);
  c.state[a]:=y; m2c.deq

## Slide 25: Parent receives Response
6. Parent receiving downgrade-to-y response
  c2m.msg=<Resp, cm, a, y, data>
   c2m.deq;
  if(m.child[c][a]=M) m.data[a]:=data;
  c.state[a]:=y;
  if(m.waitc[c][a]=(Valid x) & x≥y)
  m.waitc[c][a]:=Nothing;

## Slide 26: Child receives served Request
7. Child receiving downgrade-to-y request
  (m2c.msg=<Req, mc, a, y, - >) & (c.state[a]≤y)
   m2c.deq;

## Slide 27: Child Voluntarily downgrades
8. Child to Parent: Downgrade-to-y response (vol)
  (c.waitp[a]=Nothing) & (c.state[a]>y)
   c2m.enq(<Resp, c->m, a, y,
  (if (c.state[a]=M) then c.data[a] else - )>);
  c.state[a]:=y;

## Slide 28: Some properties
Rules 1 to 8 are complete - cover all possibilities and cannot deadlock or violate cache invariants
Our protocol maintains two important invariants:
  Directory state is always a conservative estimate of a child’s state
  Every request eventually gets a corresponding response (assuming responses cannot be blocked by requests and a request cannot overtake a response for the same address)
Starvation, that is a Load or store request is ignored indefinitely has to be prevented; Fair arbitration at the memory between requests from various caches will ensure starvation freedom.

## Slide 29: FIFO property of queues
If FIFO property is not enforced, then the protocol can either deadlock or update with wrong data
A deadlock scenario:
Child 1 requests upgrade (from I) to M (msg1)
Parent responds to Child 1 with upgrade from I to M (msg2)
Child 2 requests upgrade (from I) to M (msg2)
Parent requests Child 1 for downgrade (from M) to I (msg3)
msg3 overtakes msg2
Child 1 sees request to downgrade to I and drops it
Parent never gets a response from Child 1 for downgrade to I

## Slide 30: H and L Priority Messages
At the memory, unprocessed request messages cannot block reply messages. Hence all messages are classified as H or L priority.
  all messages carrying replies are classified as high priority
Accomplished by having separate paths for H and L priority
  In Theory: separate networks
  In Practice:
    Separate Queues
    Shared physical wires for both networks
H
L