## Slide 1
Constructive Computer Architecture
Cache Coherence
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Includes slides from L21

## Slide 2: Contributors to the course material
Arvind, Rishiyur S. Nikhil, Joel Emer, Muralidaran Vijayaraghavan
Staff and students in 6.375 (Spring 2013), 6.S195 (Fall 2012), 6.S078 (Spring 2012)
  Asif Khan, Richard Ruhler, Sang Woo Jun, Abhinav Agarwal, Myron King, Kermin Fleming, Ming Liu, Li-Shiuan Peh
External
  Prof Amey Karkare & students at IIT Kanpur
  Prof Jihong Kim & students at Seoul Nation University
  Prof Derek Chiou, University of Texas at Austin
  Prof Yoav Etsion & students at Technion

## Slide 3: Memory Consistency in SMPs
Suppose CPU-1 updates A to 200.
  write-back: memory and cache-2 have stale values
  write-through: cache-2 has a stale value
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100
200
200
Do these stale values matter?
What is the view of shared memory for programming?

## Slide 4: Maintaining Store Atomicity
Store atomicity requires all processors to see writes occur in the same order
  multiple copies of an address in various caches can cause this to be violated
To meet the ordering requirement it is sufficient for hardware to ensure:
  Only one processor at a time has write permission for a address
  No processor can load a stale copy of the data after a write to the address
       cache coherence protocols

## Slide 5: A System with Multiple Caches
M
L1
P
L1
P
L1
P
L1
P
L2
L2
L1
P
L1
P
Interconnect
Modern systems often have hierarchical caches
Each cache has exactly one parent but can have zero or more children
Logically only a parent and its children can communicate directly
Inclusion property is maintained between a parent and its children, i.e.,
a  Li  a  Li+1
Because usually
Li+1 >> Li

## Slide 6: Cache Coherence Protocols
Write request:
  the address is invalidated in all other caches before the write is performed
Read request:
  if a dirty copy is found in some cache, that value must be used by doing a write-back and then reading the memory or forwarding that dirty value directly to the reader

## Slide 7: State needed to maintain Cache Coherence
Use MSI encoding in caches where
  I means this cache does not contain the address
  S means this cache has the address but so may other caches; hence it can only be read
  M means only this cache has the address; hence it can be read and written
The states M, S, I can be thought of as an order M > S > I
  A transition from a lower state to a higher state is called an Upgrade
  A transition from a higher state to a lower state is called a Downgrade

## Slide 8: Sibling invariant and compatibility
Sibling invariant:
  Cache is in state M  its siblings are in state I
  That is, the sibling states are “compatible”
    IsCompatible(M, M) = False
    IsCompatible(M, S) = False
    IsCompatible(S, M) = False
    All other cases = True

## Slide 9: Cache State Transitions
S
M
I
store
load
write-back
invalidate
flush
store
optimizations
This state diagram is helpful as long as one remembers that each transition involves cooperation of other caches and the main memory to maintain the sibling invariants

## Slide 10: Cache Actions
On a read miss (i.e., Cache state is I):
  In case some other cache has the address in state M then write back the dirty data to Memory
  Read the value from Memory and set the state to S
On a write miss (i.e., Cache state is I or S):
  Invalidate the address in all other caches and in case some cache has the address in state M then write back the dirty data
  Read the value from Memory if necessary and set the state to M
Misses cause Cache upgrade actions which in turn may cause further downgrades or upgrades on other caches

## Slide 11: MSI protocol: some issues
It never makes sense to have two outstanding requests for the same address from the same processor/cache
It is possible to have multiple requests for the same address from different processors. Hence there is a need to arbitrate requests
On a cache miss there is a need to find out the state of other caches
A cache needs to be able to evict an address in order to make room for a different address
  Voluntary downgrade
Memory system (higher-level cache) should be able to force a lower-level cache to downgrade

## Slide 12: Directory State Encoding Two-level (L1, M) system
For each address in a cache, the directory keeps two types of info
  c.state[a] (sibling info): do c’s siblings have a copy of address a; M (means no), S (means maybe)
  m.child[ck][a] (children info): the state of child ck for address a; At most one child can be in state M
a
a
P
L1
P
L1
L1
Interconnect
<S,I,I,I>
S
P
P

## Slide 13: Directory state encoding wait states
New states needed to deal with waiting for responses:
  c.waitp[a] : Denotes if cache c is waiting for a response from its parent
    Nothing means not waiting
    Valid (M|S|I) means waiting for a response to transition to M or S or I state, respectively
  m.waitc[ck][a] : Denotes if memory m is waiting for a response from its child ck
    Nothing | Valid (M|S|I)
Cache state in L1:
    <(M|S|I), (Nothing | Valid(M|S|I))>
Directory state in home memory:
  <[(M|S|I), (Nothing | Valid(M|S|I))]>
Children’s state

## Slide 14: A Directory-based Protocol an abstract view
interconnect
PP
P
c2m
m2c
L1
p2m
m2p
m
PP
in
out
PP
P
c2m
m2c
L1
p2m
m2p
Each cache has 2 pairs of queues
  (c2m, m2c) to communicate with the memory
  (p2m, m2p) to communicate with the processor
Message format: <cmd, srcdst, a, s, data>
FIFO message passing between each (srcdst) pair except a Req cannot block a Resp
Messages in one srcdst path cannot block messages in another srcdst path
Req/Resp
address
state

## Slide 15: Processor Hit Rules
Load-hit rule
  p2m.msg=(Load a) &
  (c.state[a]>I)
 p2m.deq;
m2p.enq(c.data[a]);
Store-hit rule
    p2m.msg=(Store a v) &
  c.state[a]=M
 p2m.deq;
m2p.enq(Ack);
c.data[a]:=v;
PP
P
c2m
m2c
L1
p2m
m2p

## Slide 16: Processing misses: Requests and Responses
Cache
Upgrade req
Downgrade resp
Downgrade req
Upgrade resp
Memory
Cache
Downgrade req SI, MS, MI
Upgrade resp
IS, SM, IM Upgrade req
Downgrade resp
Downgrade req
Upgrade resp
Upgrade req
Downgrade resp

## Slide 17: Processing a Load or a Store miss incomplete
Child to Parent: Upgrade-to-y request
Parent to Child: process Upgrade-to-y request
Parent to other child caches: Downgrade-to-x request
Child to Parent: Downgrade-to-x response
Parent waits for all Downgrade-to-x responses
Parent to Child: Upgrade-to-y response
Child receives upgrade-to-y response

## Slide 18: Processing a Load miss ad hoc attempt
L1 to Parent: Upgrade-to-S request
  (c.state[a]=I) & (c.waitp[a]=Nothing)
   c.waitp[a]:=Valid S;
  c2m.enq(<Req, cm, a, S, - >);
Parent to L1: Upgrade-to-S response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,S,-> & (i≠c, IsCompatible(m.child[i][a],S))
   m2c.enq(<Resp, mc, a, S, m.data[a]>);
  m.child[c][a]:=S; c2m.deq
L1 receiving upgrade-to-S response
  m2c.msg=<Resp, mc, a, S, data>
   m2c.deq; c.data[a]:=data; c.state[a]:=S;
  c.waitp[a]:=Nothing;

## Slide 19: Processing Load miss cont.
What if (i≠c, IsCompatible(m.child[i][a],y)) is false?
Downgrade other child caches
Parent to L1: Upgrade-to-S response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,S,-> & (i≠c, IsCompatible(m.child[i][a],S))
   m2c.enq(<Resp, mc, a, S, m.data[a]>);
  m.child[c][a]:=S; c2m.deq
Parent to Child: Downgrade to S request
c2m.msg=<Req,cm,a,S,-> &
  (m.child[i][a]>S) & (m.waitc[i][a]=Nothing)
   m.waitc[i][a]:=Valid S; m2c.enq(<Req, mi, a, S, - >);
It is difficult to design a protocol in this manner

## Slide 20: Invariants for a CC-protocol design
Directory state is always a conservative estimate of a child’s state
  E.g., if directory thinks that a child cache is in S state then the cache has to be in either I or S state
For every request there is a corresponding response, though sometimes a response may have been generated even before the request was processed
Communication system has to ensure that
  responses cannot be blocked by requests
  a request cannot overtake a response for the same address
At every merger point for requests, we will assume fair arbitration to avoid starvation

## Slide 21: Complete set of cache/memory actions
Cache
1,5,8
3,5,7
Memory
2,4
2,6
1 Up req send (cache)
2 Up req proc, Up resp send (memory)
3 Up resp proc (cache)
4 Dn req send (memory)
5 Dn req proc, Dn resp send (cache)
6 Dn resp proc (memory)
7 Dn req proc, drop (cache)
8 Voluntary Dn resp (cache)

## Slide 22: Child Requests
1. Child to Parent: Upgrade-to-y Request
  (c.state[a]<y) & (c.waitp[a]=Nothing)
   c.waitp[a]:=Valid y;
  c2m.enq(<Req, cm, a, y, - >);
This is a blocking cache since we did not deque the requesting message in case of a miss

## Slide 23: Parent Responds
2. Parent to Child: Upgrade-to-y response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,y,-> & (i≠c, IsCompatible(m.child[i][a],y))
   m2c.enq(<Resp, mc, a, y,
  (if (m.child[c][a]=I) then m.data[a] else -)>);
  m.child[c][a]:=y; c2m.deq;

## Slide 24: Child receives Response
3. Child receiving upgrade-to-y response
  m2c.msg=<Resp, mc, a, y, data>
   m2c.deq;
  if(c.state[a]=I) c.data[a]:=data;
  c.state[a]:=y;
  c.waitp[a]:=Nothing;
  // the child must be waiting for a state ≤ y

## Slide 25: Parent Requests
4. Parent to Child: Downgrade-to-y Request
  c2m.msg=<Req,cm,a,y,-> &
  (m.child[i][a]>y) & (m.waitc[i][a]=Nothing)
   m.waitc[i][a]:=Valid y;
  m2c.enq(<Req, mc, a, y, - >);

## Slide 26: Child Responds
5. Child to Parent: Downgrade-to-y response
  (m2c.msg=<Req,mc,a,y,->) & (c.state[a]>y)
   c2m.enq(<Resp, c->m, a, y,
  (if (c.state[a]=M) then c.data[a] else - )>);
  c.state[a]:=y; m2c.deq

## Slide 27: Parent receives Response
6. Parent receiving downgrade-to-y response
  c2m.msg=<Resp, cm, a, y, data>
   c2m.deq;
  if(m.child[c][a]=M) m.data[a]:=data;
  m.child[c][a]:=y;
  if(m.waitc[c][a]=(Valid x) & x≥y)
  m.waitc[c][a]:=Nothing;

## Slide 28: Child receives served Request
7. Child receiving downgrade-to-y request
  (m2c.msg=<Req, mc, a, y, - >) & (c.state[a]≤y)
   m2c.deq;

## Slide 29: Child Voluntarily downgrades
8. Child to Parent: Downgrade-to-y response (vol)
  (c.waitp[a]=Nothing) & (c.state[a]>y)
   c2m.enq(<Resp, c->m, a, y,
  (if (c.state[a]=M) then c.data[a] else - )>);
  c.state[a]:=y;
Rules 1 to 8 are complete - cover all possibilities and cannot deadlock or violate cache invariants

## Slide 30: Are the rules exhaustive? Parent rules
2. Parent to Child: Upgrade-to-y response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,y,-> & (i≠c, IsCompatible(m.child[i][a],y))
   m2c.enq(<Resp, mc, a, y,
  (if (m.child[c][a]=I) then m.data[a] else -)>);
  m.child[c][a]:=y; c2m.deq;
No deq, hence the request is kept pending at the head of the queue;
The address is marked as “busy”, i.e., waiting
  What if (i≠c, IsCompatible(m.child[i][a],y)) is False?
Rule 4 will get invoked
4. Parent to Child: Downgrade-to-y Request
  c2m.msg=<Req,cm,a,y,-> &
  (m.child[i][a]>y) & (m.waitc[i][a]=Nothing)
   m.waitc[i][a]:=Valid y; m2c.enq(<Req, mi, a, y, - >);

## Slide 31: Are rules exhaustive? Parent rules
2. Parent to Child: Upgrade-to-y response
  (j, m.waitc[j][a]=Nothing) & c2m.msg=<Req,cm,a,y,-> & (i≠c, IsCompatible(m.child[i][a],y))
   m2c.enq(<Resp, mc, a, y,
  (if (m.child[c][a]=I) then m.data[a] else -)>);
  m.child[c][a]:=y; c2m.deq;
4. Parent to Child: Downgrade-to-y Request
  (m.child[i][a]>y) & (m.waitc[i][a]=Nothing)
   m.waitc[i][a]:=Valid y; m2c.enq(<Req, mc, a, y, - >);
6. Parent receiving downgrade-to-y response
  c2m.msg=<Resp, cm, a, y, data>
   c2m.deq; if(m.child[c][a]=M) m.data[a]:=data; c.state[a]:=y;
  if(m.waitc[c][a]=(Valid x) & x≥y) m.waitc[c][a]:=Nothing;
What if (j, m.waitc[j][a]=Nothing) is False?
It is OK not to process the request because this condition will eventually be cleared out

## Slide 32: Is every rule necessary?
Consider rule 7 for cache
7. Child receiving downgrade-to-y request
  (m2c.msg=<Req, mc, a, y, - >) & (c.state[a]≤y)
   m2c.deq;
Can happen because of voluntary downgrade
8. Child to Parent: Downgrade-to-y response (vol)
  (c.waitp[a]=Nothing) & (c.state[a]>y)
   c2m.enq(<Resp, c->m, a, y,
  (if (c.state[a]=M) then c.data[a] else - )>);
  c.state[a]:=y;
A downgrade request comes but the cache is already in the downgraded state

## Slide 33: More rules?
How about a voluntary upgrade rule from parent?
Parent to Child: Upgrade-to-S response (vol)
  (m.waitc[c][a]=Nothing) & (m.cstate[c][a]=S)
   m2c.enq(<Resp, m->c, a, M, -);
  m.cstate[c][a]:=M;
The child could have simultaneously evicted the line, in which case the parent eventually makes m.cstate[c][a] = I while the child makes its c.state[a] = M. This breaks our invariant
A cc protocol is like a Swiss watch, even the smallest change can easily (and usually does) introduce bugs

## Slide 34: Communication Network
Two virtual networks:
  For requests and responses from cache to memory
  For requests and responses from memory to caches
Each network has H and L priority messages - a L message can never block an H message other than that messages are delivered in FIFO order
Mem
P
L1
P
L1
L1
Interconnect
P
P
L1

## Slide 35: H and L Priority Messages
At the memory, unprocessed request messages cannot block reply messages.
H and L messages can share the same wires but must have separate queues
H
L
An L message can be processed only if H queue is empty

## Slide 36: FIFO property of queues
If FIFO property is not enforced, then the protocol can either deadlock or update with wrong data
A deadlock scenario:
Child 1 requests upgrade (from I) to M (msg1)
Parent responds to Child 1 with upgrade from I to M (msg2)
Child 2 requests upgrade (from I) to M (msg3)
Parent requests Child 1 for downgrade (from M) to I (msg4)
msg4 overtakes msg2
Child 1 sees request to downgrade to I and drops it
Parent never gets a response from Child 1 for downgrade to I

## Slide 37: Deadlocks due to buffer space
A cache or memory always accepts a response, thus responses will always drain from the network
From the children to the parent, two buffers are needed to implement the H-L priority. A child’s req can be blocked and generate more requests
From parent to all the children, just one buffer in the overall network is needed for both requests and responses because a parent’s req only generates responses

## Slide 38: Integrating PP into a non-blocking cache
St
Q
Ld
Buff
Wait
Q
V/
D/
I/
W
Tag
Data
mReqQ
mRespQ
hitQ
resp
req
PP
P
c2m
m2c
L1
p2m
m2p
Some cache rules need to be changed