## Slide 1
Constructive Computer Architecture
Tutorial 1
Andy Wright
6.S195 TA

## Slide 2: Administrative Stuff
Piazza
  Was everyone added to the class?
Lab 1 (Due Friday)
  Has everyone tried logging onto vlsifarm?
  What about checking out the lab git repositories?
  Anyone having technical problems?

## Slide 3: Bluespec Introduction
Combinational Circuits
  Written as Functions
    Problem: all functions inlined, no code reuse
  Written as Modules
    Allows for code reuse, but is more complicated
Sequential Circuits
  Requires Reg#(…)’s and Rules
    Currently the examples from lecture only use 1 rule.
    Adding multiple rules compilcates things and will be covered in a later lecture.

## Slide 4: Bluespec Types
Bool
Bit#(n)
Enum
Struct
typedef enum {
ADD,
SUB,
MUL,
DIV
} Operation deriving(Bits, Eq);
typedef struct {
Operation op;
Bit#(32) val;
} Command deriving(Bits, Eq);

## Slide 5: Bluespec Type - Tuples
Type: Tuple2#(type a, type b)
  Also Tuple3#(a,b,c) up to Tuple8#(…)
Values: tuple2( val_a, val_b )
Components: tpl_1(t), tpl_2(t), …
Tuple2#(Bool, Bit#(16)) t = tuple2( true, 4 );
Bool a_val = tpl_1(t);
Bit#(16) b_val = tpl_2(t);

## Slide 6: Bluespec Type - Vectors
Type: Vector#(numeric type size, type data_type)
Values: newVector(), replicate(val)
Elements accessed by []
Advanced functions like zip, map, and fold
  See the Bluespec Reference Manual for more info
Vector#(32, Bit#(32)) rfile_values = replicate(0);
rfile_values[7] = 5;

## Slide 7: Bluespec Type - Reg
Type: Reg#(type data_type)
Instantiated differently from normal variables
  Uses <- notation
Written to differently from normal variables
  Uses <= notation
Reg#(Bit#(32)) a_reg <- mkReg(0) // value set to 0
Reg#(Bit#(32)) b_reg <- mkRegU() // uninitialized
// write to b_reg (needs to be done inside rule)
b_reg <= 7;

## Slide 8: Reg and Vector
Register of Vectors
  Reg#( Vector#(32, Bit#(32) ) ) rfile;
  rfile <- mkReg( replicate(0) );
Vector of Registers
  Vector#( 32, Reg#(Bit#(32)) ) rfile;
  rfile <- replicateM( mkReg(0) );
Each has its own advantages and disadvantages

## Slide 9: Numeric Types
typedef 5 N; // N is the numeric type 5
Bit#(N); // Same as Bit#(5)
valueOf(N); // The Integer 5
Bit#(n); // type variable

## Slide 10: Modules
Modules are building blocks for larger systems
  Modules contain other modules and ruls
  Moduels are accessed through their interface
module mkAdder( Adder#(32) );
  Adder#(32) is the interface

## Slide 11: Interfaces
Interfaces contain methods for other modules to interact with the given module
  Interfaces can also contain other interfaces
interface MyInterface#(numeric type n);
method ActionValue#(Bit#(b)) f();
interface SubInterface s;
endinterface

## Slide 12: Interface Methods
Method
  Returns value, doesn’t change state
  method Bit#(32) peek_at_front();
Action
  Changes state, doesn’t return value
  method Action enqueue();
ActionValue
  Changes state, returns value
  method ActionValue#(Bit#(32)) dequeue_front()

## Slide 13: Strong Typing
The Bluespec Compiler throws errors if it can’t figure out a type
Which of the following lines work?
Bit#(32) a = 7; Bit#(8) small_b = 3;
let b = zeroExtend( small_b );
Bit#(32) other_b = zeroExtend( small_b );
let a_plus_b = a + zeroExtend( small_b );
Bit#(8) small_b_plus_fifty_truncated
= truncate( 50 + zeroExtend( small_b ) );

## Slide 14: WideMux Example

## Slide 15: Addition Circuits and Critical Paths

## Slide 16: Multiplication by repeated addition
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
a0
m0
a1
m1
a2
m2
a3
m3
add4
0
add4
add4
mi = (a[i]==0)? 0 : b;

## Slide 17: Design issues with combinational multiply
Lot of hardware
  32-bit multiply uses 31 add32 circuits
Long chains of gates
  32-bit ripple carry adder has a 31-long chain of gates
  32-bit multiply has 31 ripple carry adders in sequence!
The speed of a combinational circuit is determined by its longest input-to-output path
What is this path?