## Slide 1
Constructive Computer Architecture
Tutorial 3:
Debugging SMIPS
Andy Wright
6.S195 TA

## Slide 2: Introduction
In lab 4, you will be making modifications to an existing, functional, SMIPS processor
How do you know if your processor is working?
  You will run an existing suite of C and assembly software test benches on your processor
What could go wrong?
  Software and Hardware
How will you debug this?
  Print statements!

## Slide 3: SMIPS Cpu Interface

## Slide 4: SMIPS Cpu Interface
Hardware Problems
Software
Problems

## Slide 5: Running SMIPS Test Benches - Success
$ ./smips –x –b 1cyc.bsv –c all -r
…
Compiling programs/src/assembly/smipsv2_addu.S
Running smipsv2_addu.S on 1cyc.bsv
PASSED
…
Compiling programs/src/vvadd
Running vvadd on 1cyc.bsv
Cycles = 3018
Insts = 3018
PASSED
…

## Slide 6: SMIPS’s Coprocessor
The coprocessor is what enables these software tests
  Reg 10 (read): Number of clock cycles passed
  Reg 11 (read): Number of instructions executed
  Reg 18 (write): Printing an integer
  Reg 19 (write): Printing a character
  Reg 21 (write): Finished executing (data is return code)

## Slide 7: Test Benches
Test Benches can be written in assembly or in C
  Assembly examples:
    smipsv1_simple.s
    smipsv2_addu.s
  C example:
    vvadd

## Slide 8: Running SMIPS Test Benches - Failure
$ ./smips –x –b 1cyc.bsv –c all -r
…
Compiling programs/src/assembly/smipsv1_lw.S
Running smipsv2_addu.S on 1cyc.bsv
FAILED 1
…
Compiling programs/src/vvadd
Running vvadd on 1cyc.bsv
Executing unsupported instruction at pc: 00000004.
Exiting
…
We need more feedback from the processor!

## Slide 9: Test Bench Setup
mkTestBench
mkProc
hostToCpu
cpuToHost
Start
Run
Where does feedback from the processor come from in this system?

## Slide 10: Printing from the COP
mkTestBench
mkProc
hostToCpu
cpuToHost
Start
Run
Cycles = 2052
Insts = 1026
PASSED
FAILED 5
These messages are written to stderr.

## Slide 11: Printing from Bluespec: Error
mkTestBench
mkProc
hostToCpu
cpuToHost
Start
Run
$fwrite(stderr, “Executing unsupported instruction at pc: %x. Exiting\n”, pc );
This message is written to stderr.

## Slide 12: Printing from Bluespec: Message
mkTestBench
mkProc
hostToCpu
cpuToHost
Start
Run
$display(“pc: %h inst: (%h) expanded: “, pc, inst, showInst(inst));
This message is written to stdout every clock cycle.

## Slide 13: Output streams
Stderr
  Piped to stdout in the smips test script
  Contains statements printed by software and error messages
Sdtout
  Piped to build/<program_name>/simOut
  Contains debug messages about the processor status

## Slide 14: Debugging
To debug problems, look at simOut
To debug further, you can add more $display(…) statements
…
Cycle 3057 ---------------------------------
pc: 00001098 inst: (03e00008) expanded: jr ‘h1f
Cycle 3058 ---------------------------------
pc: 00000004 inst: (aaaaaaaa) expanded: nop