## Slide 1
Constructive Computer Architecture
Tutorial 5:
Overcoming SMIPS Scheduling Errors
Andy Wright
6.S195 TA

## Slide 2: Introduction
Going to talk about the SMIPS 2 stage pipeline connected by FIFOs
In the process of speeding it up, we are going to run into some scheduling errors
  To learn more about these errors we are going to use tools built into the Bluespec GUI
After we know where the scheduling errors are coming from, we are going to fix them
Fixing these scheduling errors will be very relevant to lab5!

## Slide 3: SMIPS Fetch/Execute Division
Two rules connected by fifos.
Not very fast, but can be sped up with a few additions.
doFetch
doExecute
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2

## Slide 4: SMIPS 2 Cycle Pipeline
Two sources of slowdowns:
  Control hazards
    Branch misprediction
    Seen in Lab 4
    Can be sped up with bypass redirect fifo or a better branch predictor
  Read after write (RAW) hazards
    Scoreboard forces stalling
    Can be sped up with a bypass register file

## Slide 5: SMIPS Example – RAW
reg1 <- reg2 + 13
reg2 <- reg1 - 1
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2

## Slide 6: SMIPS Example – Cycle 1
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2
reg1 <- reg2 + 13
reg1 <- reg2 + 13
reg2 <- reg1 - 1
2
1

## Slide 7: SMIPS Example – Cycle 2
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2
reg1 <- reg2 + 13
reg1 <- reg2 + 13
reg2 <- reg1 - 1
2
1
1
reg2 <- reg1 – 1
Stall due to Scoreboard!

## Slide 8: SMIPS Example – Cycle 3
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2
reg1 <- reg2 + 13
reg2 <- reg1 - 1
reg2 <- reg1 – 1
Now this instruction is free to execute

## Slide 9: SMIPS Example – Cycle 3
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2
reg1 <- reg2 + 13
reg2 <- reg1 - 1
reg2 <- reg1 – 1
2
1

## Slide 10: SMIPS Example – Cycle 4
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2
reg1 <- reg2 + 13
reg2 <- reg1 - 1
reg2 <- reg1 – 1
2
1
2

## Slide 11: SMIPS Example – Cycle 5
doFetch
doExecute
d2e
redirect
… Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
1
2
reg1 <- reg2 + 13
reg2 <- reg1 - 1

## Slide 12: Processor Enhancements
2 candidates:
  Bypass register file
    Reduces RAW hazard penalty, but it introduces a long combinational path
  Bypass redirect fifo
    Reduces misprediction penalty without increasing the critical path significantly
Bypass redirect fifo is a good first step, so lets start there.

## Slide 13: Variation 1 – Before improvements
Standard CF fifos used for fetch to execute fifo and redirect fifo
Results from simulation can be found in the orig folder in the included code

## Slide 14: Variation 1 - Results
Looking at smips.out
  No scheduling warnings
  Between 0.5 and 1.0 IPC
  On average, 1 to 2 cycles per instruction
Looking at simOut
  Long misprediction penalty
  Fetch and Execute fire at the same time

## Slide 15: Variation 2 – Shorter Misprediction Penalty?
This uses a bypass fifo for the redirect fifo in an attempt to reduce the misprediction penalty by a cycle.
Results from simulation can be found in the bad folder in the included code

## Slide 16: Variation 2 - Results
Looking at smips.out
  No scheduling warnings
  Less than 0.5 IPC
  More than 2 cycles per instruction on average
Looking at simOut
  Same misprediction penalty
  Fetch and Execute don’t fire in the same cycle

## Slide 17: Scheduling Analysis
Look at scheduling analysis presentation to see how to use the Bluespec gui to get some additional scheduling information from the compiler.

## Slide 18: Register File
The current design of the register file forces read < write
We want reads to happen functionally before writes, but we want writes to be scheduled before reads
Let’s modify the register file to be conflict free!

## Slide 19: Variation 3 – Shorter Misprediction Penalty!
This uses a CF register file to go along with the bypass fifo for the redirect fifo
Results from simulation can be found in the good folder in the included code

## Slide 20: Variation 3 - Results
Looking at smips.out
  No scheduling warnings
  Between 0.5 and 1.0 IPC
  Improvement over variations 1 and 2
Looking at simOut
  Reduced misprediction penalty
  Fetch and Execute fire in the same cycle

## Slide 21: Conclusion
We had a plan to speed up the processor, but bluespec scheduling didn’t work out
We used the bluespec gui to debug our scheduling problem
We resolved a conflicting module by making it conflict free using EHRs and a canonicalize rule
We ended up getting a faster processor!

## Slide 22: Questions?