## Slide 1
Constructive Computer Architecture
Tutorial 6:
Five Details of SMIPS Implementations
Andy Wright
6.S195 TA

## Slide 2: Introduction
Lab 6 involves creating a 6 stage pipelined SMIPS processor from a 2 stage pipeline
  This requires a lot of attention to architectural details of the processor, especially at the points of interaction between the stages.
This tutorial will cover some details of the SMIPS architecture that will be useful for the current and future labs

## Slide 3: 6 stage SMIPS pipeline
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect

## Slide 4: 5 Details
Processor State
Poisoning Instructions
ASAP Prediction Correction
Pipeline Feedback
Removing Pipeline Stages

## Slide 5: 5 Details
Processor State
Poisoning Instructions
ASAP Prediction Correction
Pipeline Feedback
Removing Pipeline Stages

## Slide 6: Processor State
The processor state is (PC, RFile, Mem)
Instructions can be seen as functions of a processor state that return the new processor state
  addi(PC, RFile, Mem) = (PC+4, RFile’, Mem)
    RFile’ is RFile updated with the result of the addi instruction
The instruction memory can be seen as a function of PC that returns Instructions
  Imem: (PC) ->
  ( (PC, Rfile, Mem) -> (PC, RFile, Mem) )

## Slide 7: Processor State
If your SMIPS processor from lab is not working:
  Was an instruction executed on the wrong processor state?
    RAW hazards
    Not using the right PC in the execute stage
  Was the wrong instruction executed?
    A wrong path instruction from branch misprediction updated the processor state

## Slide 8: Processor State
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Green blocks make up the processor state. All other state elements make sure the right processor state is used to compute instructions, and to make sure the right instructions are executed.

## Slide 9: 5 Details
Processor State
Poisoning Instructions
ASAP Prediction Correction
Pipeline Feedback
Removing Pipeline Stages

## Slide 10: Poisoning Instructions
Why poison? It’s a way to mark that an instruction should be killed at a later stage.
  This mark could be as simple as using an invalid value in a maybe data type
Instructions are poisoned when epochs don’t match
Why not kill in place?

## Slide 11: Kill-In-Place Pipeline
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Scoreboard entries need to be removed when instructions are killed.

## Slide 12: Kill-In-Place Pipeline
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Both Exec and WB try to call sb.remove(). This will cause Exec to conflict with WB. Also, the scoreboard implementation doesn’t allow out-of-order removal.

## Slide 13: Poisoning Pipeline
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Poison
Kill

## Slide 14: 5 Details
Processor State
Poisoning Instructions
ASAP Prediction Correction
Pipeline Feedback
Removing Pipeline Stages

## Slide 15: ASAP Prediction Correction
Different instructions that affect the program flow can be resolved at different times
  Absolute Jumps – Decode
  Register Jumps – RFetch
  Branches – Exec
You can save cycles on each misprediction by correcting the PC once you have computed what the next PC should have been.

## Slide 16: ASAP Prediction Correction
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
This is the general idea, we want Decode, RFetch, and Exec to be able to correct the PC

## Slide 17: ASAP Prediction Correction
How is this actually done?
How do you keep from allowing wrong path instructions to update the PC?
How do you keep track of everything?
How?
  More Epochs!

## Slide 18: ASAP Prediction Correction
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Decode, RFetch, and Exec each have their own epoch.
dEpoch
rfEpoch

## Slide 19: ASAP Prediction Correction
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Each epoch acts just like eEpoch does

## Slide 20: Correcting PC in Execute

## Slide 21: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
1
2
3
4
5
6
Mispredicted
Write Back

## Slide 22: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
2
3
4
5
6
1
Poisoning
Write Back

## Slide 23: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
3
4
5
6
1
2
Poisoning
Write Back

## Slide 24: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
4
5
6
1
2
3
Poisoning
Killing

## Slide 25: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
5
6
1
2
3
4
Executing
Killing

## Slide 26: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
6
1
2
3
4
5
Executing
Killing

## Slide 27: Correcting PC in Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
1
2
3
4
5
6
Executing
Write Back

## Slide 28: Correcting PC in Decode

## Slide 29: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
1
2
3
4
5
6
Mispredicted
Write Back

## Slide 30: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
2
3
4
5
6
1
Killing
Write Back

## Slide 31: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
3
4
5
1
2
Decoding
Write Back

## Slide 32: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
4
5
1
2
3
Decoding
Write Back

## Slide 33: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
5
1
2
3
4
Decoding
Write Back

## Slide 34: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
1
2
3
4
5
Decoding
Stall

## Slide 35: Correcting PC in Decode
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
fEpoch
PC
Redirect
dEpoch
2
3
4
5
6
Decoding
Write Back
1

## Slide 36: Correcting PC in Decode and Execute

## Slide 37: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
6
Executing
Write Back
dEpoch
Decoding
fdEpoch
feEpoch
Fetch has local estimates of eEpoch and dEpoch
Decode has a local estimate of eEpoch

## Slide 38: Correcting PC in Decode and Execute
What if decode and execute see mispredictions in the same cycle?
  If execute sees a misprediction, then the decode instruction is a wrong path instruction. The redirect coming from decode should be ignored.

## Slide 39: Correcting PC in Decode and Execute
What if execute sees a misprediction, then decode sees one in the next cycle?
  The decode instruction will be a wrong path instruction, so it should not try to redirect the PC

## Slide 40: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
6
Mispredicted
Write Back
dEpoch
Decoding
fdEpoch
feEpoch
Assume this instruction is a mispredicted jump instruction. It will be in the decode stage next cycle

## Slide 41: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
2
3
4
5
6
1
Poisoning
Write Back
dEpoch
Killing
fdEpoch
feEpoch
The decode stage knows eEpoch, and recognizes this misprediction is a wrong path instruction. The decode stage kills this instruction.

## Slide 42: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
3
4
5
1
1
Poisoning
Write Back
dEpoch
Decoding
fdEpoch
feEpoch

## Slide 43: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
4
5
1
2
3
Stalling
Killing
dEpoch
Decoding
fdEpoch
feEpoch

## Slide 44: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
5
1
2
3
4
Executing
Killing
dEpoch
Decoding
fdEpoch
feEpoch

## Slide 45: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
Executing
Stalling
dEpoch
Decoding
fdEpoch
feEpoch

## Slide 46: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
2
3
4
5
6
Executing
Write Back
dEpoch
Decoding
fdEpoch
feEpoch
1

## Slide 47: Correcting PC in Decode and Execute
What if decode sees a misprediction, then execute sees one in the next cycle?
  The decode instruction will be a wrong path instruction, but it won’t be known to be wrong path until later

## Slide 48: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
6
Executing
Write Back
dEpoch
Mispredicted
fdEpoch
feEpoch
Assume this instruction is a mispredicted branch instruction. It will be in the execute stage next cycle

## Slide 49: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
2
3
4
5
6
1
Mispredicted
Write Back
dEpoch
Killing
fdEpoch
feEpoch
The PC was just “corrected” to a different wrong path instruction

## Slide 50: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
3
4
5
1
1
Poisoning
Write Back
dEpoch
Killing
fdEpoch
feEpoch
The PC was just corrected to a correct path instruction

## Slide 51: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
4
5
1
2
Stalling
Write Back
dEpoch
Decoding
fdEpoch
feEpoch
The PC was just corrected to a correct path instruction

## Slide 52: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
5
1
2
3
Stalling
Killing
dEpoch
Decoding
fdEpoch
feEpoch
The PC was just corrected to a correct path instruction

## Slide 53: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
Executing
Stalling
dEpoch
Decoding
fdEpoch
feEpoch
The PC was just corrected to a correct path instruction

## Slide 54: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
Executing
Stalling
dEpoch
Decoding
fdEpoch
feEpoch
The PC was just corrected to a correct path instruction

## Slide 55: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
6
Executing
Write Back
dEpoch
Decoding
fdEpoch
feEpoch
The PC was just corrected to a correct path instruction

## Slide 56: 5 Details
Processor State
Poisoning Instructions
ASAP Prediction Correction
Pipeline Feedback
Removing Pipeline Stages

## Slide 57: Pipeline Feedback
You can forward changes to the processor state to later instructions in the pipeline
  Forwarding PC state
    Redirect fifo
    Epoch updates
  Forwarding register file state
    Register file data
    Scoreboard entries
  Forwarding memory state
    Covered later in class (maybe)

## Slide 58: Pipeline Feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect

## Slide 59: Pipeline Feedback
Better processor performance can be obtained by faster feedback
  EHRs can be used to make state updates appear to happen in less than a cycle
How can Epoch and PC feedback be sped up?

## Slide 60: fEpoch and PC feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Normally updates to fEpoch and PC epoch have to pass through the redirect fifo. When IFetch sees entries in the redirect fifo, it makes the changes to fEpoch and PC

## Slide 61: fEpoch and PC feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
Epoch [0]
Epoch [1]
PC
Redirect
Changes to the Epoch can now be seen by IFetch in the same cycle that execute made the changes

## Slide 62: fEpoch and PC feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
Epoch [0]
Epoch [1]
PC
Redirect
The PC is still coming through the redirect fifo, so the epoch and the pc will get out of synch!

## Slide 63: fEpoch and PC feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
Epoch [0]
Epoch [1]
PC [1]
Make the PC an EHR too! Whenever Execute sees a misprediction, IFetch reads the correct next instruction in the same cycle!
PC [0]

## Slide 64: Pipeline Feedback
How can Register File and Scoreboard feedback be sped up?

## Slide 65: RFile and SB feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Normally updates (writes) to the register file and updates (removes) to the scoreboard are seen in the next cycle.

## Slide 66: RFile and SB feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Bypass Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
A bypass register file will allow the result from a write to be read by RFetch in the same cycle.

## Slide 67: RFile and SB feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Bypass Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
In this case, the scoreboard is still stalling as much as before

## Slide 68: RFile and SB feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Bypass Register File
Pipeline Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
You can use a scoreboard that removes before searching (called a pipeline scoreboard because it is similar to pipeline fifo’s deq<enq behavior)

## Slide 69: 5 Details
Processor State
Poisoning Instructions
ASAP Prediction Correction
Pipeline Feedback
Removing Pipeline Stages

## Slide 70: Removing Pipeline Stages
You will create a 6 stage SMIPS pipeline in Lab 6
  6 is a lot of stages and may not be necessary
  How much work would it be to turn it into a shorter pipeline? Say 4 stages?
  How much work would it be to shift work from one pipeline stage to another?

## Slide 71: Removing Pipeline Stages
IFetch
Decode
WB
Exec
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Say you want a 4 stage pipeline where Decode does RFetch and Exec does Memory. How do you make this machine with as little work as possible?

## Slide 72: Removing Pipeline Stages
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Replace CFFifos between stages with bypass fifos. The bypass fifos will act as wires when possible.
Bypass Fifos

## Slide 73: Removing Pipeline Stages
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Now you want to move RFetch to the Exec stage to reduce the amount of time stalled for RAW hazards. How much work is this?

## Slide 74: Removing Pipeline Stages
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Just change the types of fifos between Decode and RFetch and between RFetch and Exec.

## Slide 75: Removing Pipeline Stages
The 6 stage pipeline is very flexible.
You can try out many different stage configurations in FPGA synthesis to see how your IPS (Instructions Per Seconds) changes.

## Slide 76: Conclusion
Processor State
  Most processor errors can be related to operating on the wrong processor state
Poisoning Instructions
  Needed for lab 6
ASAP Prediction Correction
  This will be covered in more depth in lab 7.
Pipeline Feedback
  Can be used to speed up processors
Removing pipeline stages
  Can also be used to speed up processors

## Slide 77: Questions?