## Slide 1
Constructive Computer Architecture
Tutorial 7:
SMIPS Labs and Epochs
Andy Wright
6.S195 TA

## Slide 2: Introduction
Lab 6
  6 Stage SMIPS Processor
  Due today
Lab 7
  Complex Branch Predictors
  Posted online
  Due next Friday

## Slide 3: Lab 6
Does low IPC => low grade?
  Only if low IPC is from a ‘mistake’ in your processor.
What is a ‘mistake’?
  Not updating your BTB with redirect information
  Using too small of a scoreboard
  Having schedule conflicts between pipeline stages

## Slide 4: Lab 6
What questions do you have?

## Slide 5: Lab 7
Adding history bits to BTB
  Combines target and direction prediction
Implement BHT
  Separates direction prediction from target prediction
Synthesize for FPGA
  Used to calculate IPS

## Slide 6: Fixed slides from L16
Epoch Management

## Slide 7: Multiple predictors in a pipeline
At each stage we need to take two decisions:
  Whether the current instruction is a wrong path instruction. Requires looking at epochs
  Whether the prediction (ppc) following the current instruction is good or not. Requires consulting the prediction data structure (BTB, BHT, …)
Fetch stage must correct the pc unless the redirection comes from a known wrong path instruction
Redirections from Execute stage are always correct, i.e., cannot come from wrong path instructions

## Slide 8: Dropping or poisoning an instruction
Once an instruction is determined to be on the wrong path, the instruction is either dropped or poisoned
Drop: If the wrong path instruction has not modified any book keeping structures (e.g., Scoreboard) then it is simply removed
Poison: If the wrong path instruction has modified book keeping structures then it is poisoned and passed down for book keeping reasons (say, to remove it from the scoreboard)
Subsequent stages know not to update any architectural state for a poisoned instruction

## Slide 9: N-Stage pipeline – BTB only
recirect
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
fEpoch
At Execute:
  (pc) if (epoch!=eEpoch) then mark instruction as poisoned
  (ppc) if (no poisoning) & mispred then change eEpoch; send <pc, newPc, ...> to Fetch
At Fetch:
  msg from execute: train BTB with <pc, newPc, taken, mispredict>
  if msg from execute indicates misprediction then set pc, change fEpoch
attached to every fetched instruction
{pc, ppc, epoch}
eEpoch
{pc, newPc, taken mispredict, ...}
BTB
...
Notes: 9
In a similar way to FXep and Xep, we distribute Dep into Dep and FDep.

## Slide 10: N-Stage pipeline: Two predictors
Suppose both Decode and Execute can redirect the PC; Execute redirect should have priority, i.e., Execute redirect should never be overruled
We will use separate epochs for each redirecting stage
  feEpoch and deEpoch are estimates of eEpoch at Fetch and Decode, respectively
  fdEpoch is Fetch’s estimates of dEpoch
  Initially set all epochs to 0
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
redirect PC
redirect PC
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...

## Slide 11: N-Stage pipeline: Two predictors Redirection logic
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...
At execute:
  (pc) if (ieEp!=eEp) then poison the instruction
  (ppc) if (no poisoning) & mispred then change eEp;
  (ppc) for every control instruction send <pc, target pc, taken, mispred…> to fetch
At fetch:
  msg from execute: if (mispred) set pc, change feEp,
  msg from decode: If (no redirect message from Execute)
  if (ideEp=feEp) then set pc, change fdEp to idEp
At decode: …
{..., ieEp}
{pc, ppc, ieEp, idEp}
{pc, newPc, taken mispredict, ...}
{pc, newPc, idEp, ideEp...}
make sure that the msg from Decode is not from a wrong path instruction

## Slide 12: Decode stage Redirection logic
Execute
d2e
Decode
f2d
Fetch
PC
miss
pred?
miss
pred?
deEpoch
eEpoch
feEpoch
eRecirect
fdEpoch
dEpoch
dRecirect
...
{..., ieEp}
{pc, ppc, ieEp, idEp}
{pc, newPc, taken mispredict, ...}
{pc, newPc, idEp, ideEp...}
Is ieEp = deEp ?
Is idEp = dEp ?
Current instruction is OK but
Execute has redirected the pc;
Set <deEp, dEp> to <ieEp, idEp>
check the ppc prediction via BHT,
Switch dEp if misprediction
yes
no
yes
no
Current instruction is OK; check the ppc prediction via BHT, Switch dEp if misprediction
Wrong path instruction; drop it

## Slide 13: Another way to manage epochs
Write the rules as simple as possible (guarded atomic actions), then add EHRs if necessary

## Slide 14: Fetch Rule
fInst.pc = pc;
fInst.ppc = prediction( pc );
fInst.eEpoch = eEpoch;
fInst.dEpoch = dEpoch;
…
pc <= fInst.ppc;
f2dFifo.enq( fInst );

## Slide 15: Decode Rule
if( dInst.eEpoch != eEpoch )
kill fInst
else if( dInst.dEpoch != dEpoch )
kill fInst
else begin
let newpc = prediction( dInst );
if( newpc != dInst.ppc ) begin
pc <= newpc
dEpoch <= !dEpoch;
end
…
end

## Slide 16: Execute Rule
if( eInst.eEpoch != eEpoch )
poison eInst
else begin
if( mispredict ) begin
pc <= newpc;
eEpoch <= !eEpoch;
train branch predictors
end
…
end

## Slide 17: Conflicts
PC read < PC write
  fetch < {decode, execute}
dEpoch read < dEpoch write
  fetch < decode
eEpoch read < eEpoch write
  {fetch, decode} < execute
PC write C PC write
  fetch C decode C execute C fetch
None of these stages can execute in the same clock cycle!

## Slide 18: Now add EHRs
Choose an ordering between the rules and assign the corresponding EHR ports
  (fetch, decode, execute)
Change conflicting registers into EHRs
  (pc)
Ehr#(3, Addr) pc -> mkEhr(?);

## Slide 19: Fetch Rule – port 0
fInst.pc = pc[0];
fInst.ppc = prediction( pc[0] );
fInst.eEpoch = eEpoch;
fInst.dEpoch = dEpoch;
…
pc[0] <= fInst.ppc;
f2dFifo.enq( fInst );

## Slide 20: Decode Rule – port 1
if( dInst.eEpoch != eEpoch )
kill fInst
else if( dInst.dEpoch != dEpoch )
kill fInst
else begin
let newpc = prediction( dInst );
if( newpc != dInst.ppc ) begin
pc[1] <= newpc;
dEpoch <= !dEpoch;
end
…
end

## Slide 21: Execute Rule – port 2
if( eInst.eEpoch != eEpoch )
poison eInst
else begin
if( mispredict ) begin
pc[2] <= newpc;
eEpoch <= !eEpoch;
train branch predictors
end
…
end

## Slide 22: Another Ordering
Choose an ordering between the rules and assign the corresponding EHR ports
  (execute, decode, fetch)
Change conflicting registers into EHRs
  (pc, dEpoch, eEpoch)
Ehr#(3, Addr) pc -> mkEhr(?);
Ehr#(3, Bool) dEpoch -> mkEhr(False);
Ehr#(3, Bool) eEpoch -> mkEhr(False);

## Slide 23: Fetch Rule – port 2
fInst.pc = pc[2];
fInst.ppc = prediction( pc[2] );
fInst.eEpoch = eEpoch[2];
fInst.dEpoch = dEpoch[2];
…
pc[2] <= fInst.ppc;
f2dFifo.enq( fInst );

## Slide 24: Decode Rule – port 1
if( dInst.eEpoch != eEpoch[1] )
kill fInst
else if( dInst.dEpoch != dEpoch[1] )
kill fInst
else begin
let newpc = prediction( dInst );
if( newpc != dInst.ppc ) begin
pc[1] <= newpc;
dEpoch[1] <= !dEpoch[1];
end
…
end

## Slide 25: Execute Rule – port 0
if( eInst.eEpoch != eEpoch[0] )
poison eInst
else begin
if( mispredict ) begin
pc[0] <= newpc;
eEpoch[0] <= !eEpoch[0];
train branch predictors
end
…
end

## Slide 26: Different View of EHR
This transformation makes more sense when you think of an EHR as sub-cycle register.
This is explained more in the paper “The Ephemeral History Register: Flexible Scheduling for Rule-Based Designs” by Daniel L. Rosenband

## Slide 27: Questions?

## Slide 29: 6 stage SMIPS pipeline
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect

## Slide 30: Poisoning Pipeline
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
Poison
Kill

## Slide 31: Correcting PC in Decode and Execute
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
eEpoch
feEpoch
PC
Redirect
1
2
3
4
5
6
Executing
Write Back
dEpoch
Decoding
fdEpoch
feEpoch
Fetch has local estimates of eEpoch and dEpoch
Decode has a local estimate of eEpoch

## Slide 32: fEpoch and PC feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Register File
Scoreboard
DMem
IMem
Epoch [0]
Epoch [1]
PC [1]
Make the PC an EHR too! Whenever Execute sees a misprediction, IFetch reads the correct next instruction in the same cycle!
PC [0]

## Slide 33: RFile and SB feedback
IFetch
Decode
WB
RFetch
Exec
Memory
Bypass Register File
Pipeline Scoreboard
DMem
IMem
eEpoch
fEpoch
PC
Redirect
You can use a scoreboard that removes before searching (called a pipeline scoreboard because it is similar to pipeline fifo’s deq<enq behavior)