## Slide 1
Constructive Computer Architecture
Tutorial 8:
FPGA Synthesis
Andy Wright
6.S195 TA

## Slide 2: Lab Update
FPGAs are working again
  If you have any problems with them, let me know

## Slide 3: Xilinx Tool Flow
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
Programfpga
FPGA Board

## Slide 4: Xilinx Tool Flow
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
Bluespec
Xilinx
Scemi
Constraints

## Slide 5: Xilinx Reports
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
*.srp
*_map.mrp
*.par
Timing Analysis
*.twr

## Slide 6: Xilinx Reports
*.srp
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
*_map.mrp
*.par
Timing Analysis
*.twr

## Slide 7: mkBridge.srp
Search for: “Low Level Synthesis”
  You’ll see some optimizations performed such as removing constant value registers.
  This portion removes unwanted overhead of EHRs

## Slide 8: Low Level Optimizations
Enq
Canon
0
1
0
Assume this fires every cycle
0
Register always 0

## Slide 9: Low Level Optimizations
Enq
Canon
0
This can still be optimized

## Slide 10: Low Level Optimizations
Enq
Canon
No overhead from using an EHR

## Slide 11: mkBridge.srp
Search for: “current_clk1”
  This will show up in a few places, but the interesting one is in a line starting with “Timing constraint”
  You’ll find the max clock period and the critical path for the clock.
  You will also find information about other clocks.
Why is there more than 1 clock?

## Slide 12: Different Clocks
SCEMI Interface
mkProc
Phased Lock Loop (PLL)
PCIE
Ref CLK
Clocks
current_clk1

## Slide 13: Critical Path
Critical path example:
=========================================================================
Timing constraint: Default period analysis for Clock 'scemi_clk_port_clkgen/current_clk1'
Clock period: 9.874ns (frequency: 101.277MHz)
Total number of paths / destination ports: 114672315 / 13117
-------------------------------------------------------------------------
Delay: 9.874ns (Levels of Logic = 17)
Source: scemi_dut_dut_dutIfc_m_dut/m/rf2eFifo_data_1_96 (FF)
Destination: scemi_dut_dut_dutIfc_m_dut/m/brpred/arr/Mram_arr1 (RAM)
Source Clock: scemi_clk_port_clkgen/current_clk1 rising
Destination Clock: scemi_clk_port_clkgen/current_clk1 rising
Data Path: scemi_dut_dut_dutIfc_m_dut/m/rf2eFifo_data_1_96 to scemi_dut_dut_dutIfc_m_dut/m/brpred/arr/Mram_arr1
...
m is mkProc
logic
rf2eFifo
brpred
?

## Slide 14: Critical Path
Gate Net
Cell:in->out fanout Delay Delay Logical Name (Net Name)
---------------------------------------- ------------
FDE:C->Q 1 0.471 0.710 rf2eFifo_data_1_96 (rf2eFifo_data_1_96)
LUT3:I0->O 55 0.094 0.468 eRVal1__h82702<31>1 (eRVal1__h82702<31>)
begin scope: 'instance_exec_1'
begin scope: 'instance_aluBr_0'
INV:I->O 2 0.238 0.581 Mmux_aluBr_not00011_INV_0 (...)
LUT2:I0->O 1 0.094 0.000 Mcompar_aluBr_a_SLE_0___d6_lut<6> (...)
MUXCY:S->O 1 0.600 0.576 Mcompar_aluBr_a_SLE_0___d6_cy<6> (...)
LUT6:I4->O 28 0.094 0.607 Mmux_aluBr61 (aluBr)
end scope: 'instance_aluBr_0'
begin scope: 'instance_brAddrCalc_2'
LUT5:I4->O 6 0.094 0.737 brAddrCalc<0>11 (N01)
LUT5:I2->O 2 0.094 0.715 brAddrCalc<27> (brAddrCalc<27>)
end scope: 'instance_brAddrCalc_2‘
...
logic
rf2eFifo
brpred
?
Branch Target Calculation

## Slide 15: Critical Path
Gate Net
Cell:in->out fanout Delay Delay Logical Name (Net Name)
---------------------------------------- ------------
LUT6:I3->O 1 0.094 0.000 Mcompar_IF_..._d32_cmp_ne0000_lut<9> (...)
MUXCY:S->O 1 0.372 0.000 Mcompar_IF_..._d32_cmp_ne0000_cy<9> (...)
MUXCY:CI->O 3 0.254 0.491 Mcompar_IF_..._d32_cmp_ne0000_cy<10> (...)
end scope: 'instance_exec_1'
LUT6:I5->O 196 0.094 0.638 redirectFifo_data_0_lat_0_whas11 (...)
LUT6:I5->O 65 0.094 0.613 CASE_y5239_0_IF_redirectFifo_data_... (...)
begin scope: 'brpred'
LUT2:I1->O 56 0.094 0.468 arr_WE1 (tagArr_WE)
begin scope: 'arr'
RAM64M:WE 0.490 Mram_arr1
----------------------------------------
Total 9.874ns (3.271ns logic, 6.603ns route)
(33.1% logic, 66.9% route)
logic
rf2eFifo
brpred
?
Redirect Fifo
Branch Predictor

## Slide 16: Critical Path
Gate Net
Cell:in->out fanout Delay Delay Logical Name (Net Name)
---------------------------------------- ------------
LUT6:I3->O 1 0.094 0.000 Mcompar_IF_..._d32_cmp_ne0000_lut<9> (...)
MUXCY:S->O 1 0.372 0.000 Mcompar_IF_..._d32_cmp_ne0000_cy<9> (...)
MUXCY:CI->O 3 0.254 0.491 Mcompar_IF_..._d32_cmp_ne0000_cy<10> (...)
end scope: 'instance_exec_1'
LUT6:I5->O 196 0.094 0.638 redirectFifo_data_0_lat_0_whas11 (...)
LUT6:I5->O 65 0.094 0.613 CASE_y5239_0_IF_redirectFifo_data_... (...)
begin scope: 'brpred'
LUT2:I1->O 56 0.094 0.468 arr_WE1 (tagArr_WE)
begin scope: 'arr'
RAM64M:WE 0.490 Mram_arr1
----------------------------------------
Total 9.874ns (3.271ns logic, 6.603ns route)
(33.1% logic, 66.9% route)
rf2eFifo
brpred
Redirect Fifo
Branch Predictor
redirectFifo
branch target calculation
Bypass Fifo
Combinational Path

## Slide 17: Splitting Critical Paths
rf2eFifo
brpred
redirectFifo
branch target calculation
Way 1:
rf2eFifo
brpred
redirectFifo
branch target calculation
Bypass Fifo
CF Fifo
(potential) new critical path
pc
This will slow down PC redirection!

## Slide 18: Splitting Critical Paths
rf2eFifo
brpred
redirectFifo
branch target calculation
Way 2:
rf2eFifo
brpred
redirectFifo
branch target calculation
Bypass Fifo
New CF Fifo
pc
(potential) new critical path
This will only slow brpred training

## Slide 19: Critical Path
After splitting the critical path with way 1:
=========================================================================
Timing constraint: Default period analysis for Clock 'scemi_clk_port_clkgen/current_clk1'
Clock period: 8.749ns (frequency: 114.294MHz)
Total number of paths / destination ports: 38299383 / 13320
-------------------------------------------------------------------------
Delay: 8.749ns (Levels of Logic = 19)
Source: scemi_dut_dut_dutIfc_m_dut/m/rf2eFifo_data_1_96 (FF)
Destination: scemi_dut_dut_dutIfc_m_dut/m/rf2eFifo_enqEn_rl (FF)
Source Clock: scemi_clk_port_clkgen/current_clk1 rising
Destination Clock: scemi_clk_port_clkgen/current_clk1 rising
Data Path: scemi_dut_dut_dutIfc_m_dut/m/rf2eFifo_data_1_96 to scemi_dut_dut_dutIfc_m_dut/m/rf2eFifo+enqEn+rl
rf2eFifo
brpred
redirectFifo
branch target calculation
CF Fifo

## Slide 20: Xilinx Reports
*.srp
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
*_map.mrp
*.par
Timing Analysis
*.twr

## Slide 21: mkBridge_map.mrp
Search for: “Design Summary”
  You’ll see how much of the FPGAs resources are being used by your designs.
  This information reveals how big your design is and how much routing congestion to expect.

## Slide 22: LUT-FF Pair
LUT
Inputs | OA | OB
00000 | 0 | 0
00001 | 1 | 1
00010 | 1 | 0
... |  | 
11111 | 1 | 1
OB
1
OA
0
Programming the FPGA sets these bits
This is a simplified version of LUT-FF Pairs

## Slide 23: Design Summary
Slice Logic Utilization:
Number of Slice Registers: 11,697 out of 69,120 16%
Number used as Flip Flops: 11,693
Number used as Latches: 1
Number used as Latch-thrus: 3
Number of Slice LUTs: 17,958 out of 69,120 25%
Number used as logic: 17,392 out of 69,120 25%
Number using O6 output only: 16,372
Number using O5 output only: 613
Number using O5 and O6: 407
Number used as Memory: 520 out of 17,920 2%
Number used as Dual Port RAM: 376
Number using O6 output only: 136
Number using O5 output only: 3
Number using O5 and O6: 237
Number used as Shift Register: 144
Number using O6 output only: 144
Number used as exclusive route-thru: 46
Number of route-thrus: 715
Number using O6 output only: 653
Number using O5 output only: 57
Number using O5 and O6: 5
Total number used
Total number on FPGA
Using about the quarter of the chip’s resources

## Slide 24: FPGA Slice
LUT
LUT
LUT
LUT
LUT-FF Pair

## Slide 25: Design Summary
Slice Logic Distribution:
Number of occupied Slices: 7,385 out of 17,280 42%
Number of LUT Flip Flop pairs used: 21,432
Number with an unused Flip Flop: 9,735 out of 21,432 45%
Number with an unused LUT: 3,474 out of 21,432 16%
Number of fully used LUT-FF pairs: 8,223 out of 21,432 38%
Number of unique control sets: 881
Number of slice register sites lost
to control set restrictions: 1,953 out of 69,120 2%
IO Utilization:
Number of bonded IOBs: 11 out of 640 1%
Number of LOCed IOBs: 11 out of 11 100%
Number of bonded IPADs: 4
Number of LOCed IPADs: 2 out of 4 50%
Number of bonded OPADs: 2
Using about half of the chip’s area

## Slide 26: Design Summary
Specific Feature Utilization:
Number of BlockRAM/FIFO: 140 out of 148 94%
Number using BlockRAM only: 140
Total primitives used:
Number of 36k BlockRAM used: 140
Total Memory used (KB): 5,040 out of 5,328 94%
Number of BUFG/BUFGCTRLs: 8 out of 32 25%
Number used as BUFGs: 8
Number of BUFDSs: 1 out of 8 12%
Number of LOCed BUFDSs: 1 out of 1 100%
Number of GTP_DUALs: 1 out of 8 12%
Number of LOCed GTP_DUALs: 1 out of 1 100%
Number of PCIEs: 1 out of 1 100%
Number of LOCed PCIEs: 1 out of 1 100%
Number of PLL_ADVs: 2 out of 6 33%
Using almost all of the chip’s BRAM
This could be a problem

## Slide 27: Block Ram
Dedicated memory slices on FPGA
Can contain 32Kb of data per BRAM
Evenly distributed across FPGA fabric
We have 2048 Kb of instruction and data memory.
How does this fit on 32 Kb blocks?

## Slide 28: Single Block Ram
BRAM
32 Kb
Addr
Write
Data
Out
Registers on input so more combinational delay for output than input

## Slide 29: Large Block Ram: Reading
BRAM
32 Kb
BRAM
32 Kb
BRAM
32 Kb
BRAM
32 Kb
x64
Addr
lsb
Out
msb
This adds a lot more logic and routing!

## Slide 30: Large Block Ram: Writing
BRAM
32 Kb
BRAM
32 Kb
BRAM
32 Kb
BRAM
32 Kb
x64
Addr
Data
Write
lsb
Address Decoder
msb
This also adds a lot more logic and routing!

## Slide 31: Xilinx Reports
*.srp
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
*_map.mrp
*.par
Timing Analysis
*.twr

## Slide 32: mkBridge.par
Search for: “Deive Utilization Summary”
  You’ll see a more accurate report of resource utilization

## Slide 33: mkBridge_map.mrp
Search for: “Generating Clock Report”
  You’ll see some information about clock timing constraints
  All of these constraints relate to internal SceMi clocks

## Slide 34: Clock Report
----------------------------------------------------------------------------------------------------------
Constraint | Check | Worst Case | Best Case | Timing | Timing
| | Slack | Achievable | Errors | Score
----------------------------------------------------------------------------------------------------------
* TS_scemi_pcie_ep_pcie_ep0_pcie_blk_clocki | SETUP | -0.047ns| 16.188ns| 1| 47
ng_i_clkout1_1 = PERIOD TIMEGRP " | HOLD | 0.031ns| | 0| 0
scemi_pcie_ep_pcie_ep0_pcie_blk_clocking_ | | | | |
i_clkout1_1" TS_MGTCLK * 0.625 HI | | | | |
GH 50% | | | | |
----------------------------------------------------------------------------------------------------------
TS_scemi_pcie_ep_pcie_ep0_pcie_blk_clocki | SETUP | 0.045ns| 3.955ns| 0| 0
ng_i_clkout0_1 = PERIOD TIMEGRP " | HOLD | 0.418ns| | 0| 0
scemi_pcie_ep_pcie_ep0_pcie_blk_clocking_ | MINPERIOD | 0.000ns| 4.000ns| 0| 0
i_clkout0_1" TS_MGTCLK * 2.5 HIGH | | | | |
50% | | | | |
----------------------------------------------------------------------------------------------------------
TS_scemi_pcie_ep_pcie_ep0_pcie_blk_clocki | MINPERIOD | 0.000ns| 4.000ns| 0| 0
ng_i_clkout0_0 = PERIOD TIMEGRP " | | | | |
scemi_pcie_ep_pcie_ep0_pcie_blk_clocking_ | | | | |
i_clkout0_0" TS_SYSCLK * 2.5 HIGH | | | | |
50% | | | | |
This report shows internal SceMi timing errors
Asterisk (*)
Negative slack

## Slide 35: Setup and Hold
CLK
D
Q
Hold Time
Setup Time
CLK
D
Q

## Slide 36: Setup and Hold
CLK
D
Q
Min Hold Time
Min Setup Time
CLK
D
Q
Positive Slacks

## Slide 37: Setup and Hold
CLK
D
Q
Timing Error!
CLK
D
Q
Negative Slack
Min Setup Time

## Slide 38: Xilinx Reports
*.srp
*.bsv
*.v
Bluespec Compiler
HDL Compiler
RTL
NCD
FPGA Slice
Mapping
Place & Route
Final Design
Bitgen
010010110101…
*_map.mrp
*.par
Timing Analysis
*.twr

## Slide 39: mkBridge.twr
More timing information
  All about internal SceMi Clocks
  No information about current_clk1

## Slide 40: Conclusion
Any Questions?

## Slide 41: ‘build’ utility
Automates the Xilinx tool flow
See `build --doc` for more information

## Slide 42: ‘build’ utility
Performs the following stages in order:
  delete_build_dirs
  make_build_dirs
  compile_for_verilog (bsc –verilog)
  generate_scemi_parameters
  xilinx_cleanup
  make_xilinx_directory
  create_ucf_file
  create_xcf_file
  create_scr_file
  prepare_project_files
  xst_compile
  translate_and_build
  map_to_device
  place_and_route
  timing_analysis
  gen_bit_file
  timing_check
  gen_ace_file

## Slide 43: ‘build’ utility
Major stages
  compile_for_verilog
  xst_compile
  translate_and_build
  map_to_device
  place_and_route
  timing_analysis
  gen_bit_file
  timing_check