## Slide 1
Computation Structures Group
MIT’s RISCY Expedition
Andy Wright, Sizhuo Zhang, Thomas Bourgeat, Amol Bhave, Jamey Hicks, Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
RISC V Workshop, Redwood Shores, CA
January 6, 2015
Notes: 1) Introduction – We have a processor (4 minutes)
-It was tandem verified with spike
-The ISA spec had room for additional specification
2) The Expedition – We are doing stuff to it (5 minutes)
3) The Plan – How we will succeed (3 minutes)
-We are leveraging Bluespec
-We have a diverse team

## Slide 2: Introduction
We made an 64-bit RISC-V processor
  IMAFD extensions
  Machine, Supervisor, and User modes
  Boots RISC-V Linux with Sv39 Paged Virtual Memory
  Tandem verified with Spike
  Written in Bluespec System Verilog
We are using this as a base for our “Riscy Expedition”

## Slide 3: Riscy Expedition
Formal specification of the ISA
  using an operational model
Formally verified processor implementations
Memory Consistency Models
  Should RISC V have a weak memory model?
  Which memory model?
Accelerators
Microarchitecture exploration
VLSI implementations using standard ASIC flow – “push button” synthesis
  Processors tuned for ASIC designs
Notes: Our Riscy Expedition has six directions of exploration.
Formal Specification, Formal Verification, Memory Consistency Model, Accelerators, Architecture, and ASIC Implementations.
Some directions are from research interests of members in our group and some directions were decided as necessary when developing the base processor.
The rest of this presentation will be an overview of the base processor and how the expedition directions are expanding it.

## Slide 4: Verified Design
Our Philosophy: Get a working processor first, figure out why it is slow, and make it faster without breaking it
There is no separation of Design and Verification – There’s just verified design
Currently we are using Tandem Verification*
In our expedition we are moving to Formal Verification
* Technology developed by Bluespec Inc

## Slide 5: Tandem verification
Spike
RiscyFpga
HTIF
HTIF
S contains :
The pc at step n.
The instruction executed at step n
The operands and the concerned registers
The packets exchanged with HTIF, if exists
The memory operations wanted to be performed, if exists
…
…
Jmp a;
…
…
Jmp a;
…
pc
pc
Very useful but for highly-parameterized designs it provides only a weak sense of correctness
Synchronized

## Slide 6: Formal Verification and Specification
Formal Verification is constructing a proof that a processor matches a formal specification
  But we need a formal specification for RISC-V
In the ISA there are lots of (odd) cases that need to be specified for a formal verification
  Are referenced bits in page table entries set for speculatively accessed pages?
  A single instruction can result in up to 13 effective memory accesses. How exactly do they interact with each other?
    How does they influence the memory model?

## Slide 7: Memory Consistency Model
Strong consistency models (e.g. SC, TSO)
  Easy to understand, but restricts optimizations
Weak consistency models
  Permit HW optimizations, but difficult to understand
  Release Consistency (RC)
    Defined with “operation performed with respect to certain processor”
  Power/ARM
    Definition in official ISA is not clear
    General description: no ordering should be assumed
    Special cases where ordering is enforced
      Dependent loads cannot be reordered
Notes: Existing models are not satisfactory.
RC is hard to understand because it is defined using “with respect to”
Power/ARM is hard to understand because (1) official definition not clear (2) special cases where ordering is enforced.
Dependent load example:
P0: W[a] = 1; sync; W[b] = 1
P1: r1 = R[b]; r2 = R[r1-1+a]
Prohibited result: r1=1, r2 = 0

## Slide 8: We want Simple operational definitions
Legal behaviors must be observable on a simple abstract machine consisting of cores and a shared monolithic memory
Cores execute one instruction at a time in program order
  May have local buffers, like the store buffer used to define TSO; useful in modeling implicit reordering of memory instructions
  The effect of Fence instructions is to flush local buffers
Multi-ported monolithic memory which processes one read or write immediately
Notes: We want to say WMM is
Easy to understand
Relaxed enough to enable all optimizations

## Slide 9: WMM: A new weak consistency model
WMM is defined using a store buffer and an invalidation buffer per core
  Permits all load-store reorderings except stores overtaking loads
  Allows almost all microarchitectural optimizations
    out-of-order execution
    memory dependency speculation
    load-value speculation
  Provides an easy to understand operational model between cores
Notes: We want to say WMM is
Easy to understand
Relaxed enough to enable all optimizations

## Slide 10: “Flavored” Memory Accesses
Inst. Fetch
Mem.
Exec.
TLB
TLB
Instruction Fetch (I)
Virtual Address Translation (VAT)
Data Access (D)
Input/Output (IO)
This looks like 4 separate cores accessing the same memory

## Slide 11: Flavored Memory Synchronization
SFENCE.VM
  D.ST < SFENCE.VM < VAT.LD
    VAT.LD must see result of D.ST
  With this specification, some SFENCE.VMs are missing from the Linux kernel
No instruction for the other direction (yet)
  VAT.ST < ? < D.LD
  So does D.LD always need to see the results of all previous VAT.STs immediately?
We are looking at these flavored accesses closely and incorporating them into the memory model

## Slide 12: Further Work
Accelerators
  Convolutional Neural Network accelerator in BlueDBM
Microarchitecture
  Out-of-order execution multicore processor
ASIC Implementation
  Processor building blocks tuned for ASIC performance

## Slide 13: Questions?
Contact information:
  Andy Wright – acwright@mit.edu
  csg.csail.mit.edu/riscy-e