## Slide 1: 6.5930/1 Hardware Architectures for Deep Learning Dataflow for DNN Accelerator Architectures (Part 2)
Joel Emer and Vivienne Sze Massachusetts Institute of Technology Electrical Engineering & Computer Science
March 13, 2024

## Slide 2: 1-D Convolution
S
Weights
W
Inputs
Q = W-ceil(S/2)†
Outputs
*
=
int i[W]; # Input activations
int f[S]; # Filter weights
int o[Q]; # Output activations
for s in [0, S):
for q in [0, Q):
o[q] += i[q+s]*f[s]
What dataflow is this?
Weight stationary
† Assuming: ‘valid’ style convolution

## Slide 3: Weight Stationary - Animation
Notes: Note how some combinations of input activations and weights never occur.

## Slide 4: Weight Stationary - Spacetime

## Slide 5: 1-D Convolution Einsum + WS
Traversal order (fastest to slowest): Q, S
WS design for parallel weights
Traversal order (fastest to slowest):
Q
Parallel Ranks:
S
Serial WS design
Einsum:
Einsum:
Can you write the loop nest?
I hope so 😊

## Slide 6: Parallel Weight Stationary - Animation
Notes: Highlight color shows the PE that is doing the work.
What can you see in this behavior:
All weights used
Activations are multicast to all PEs
Multiple outputs are worked on and then they move to the next PE

## Slide 7: Loop Nest: NVDLA (simplified)
M = 8; C = 3;
R = 2; S = 2
P = 2; Q = 2
int i[C,H,W]; # Input activations
int f[M,C,R,S]; # Filter weights
int o[M,P,Q]; # Output activations
for r in [0,R):
for s in [0,S):
for p in [0,P):
for q in [0,Q):
parallel-for m in [0, M):
parallel-for c in [0, C):
o[m,p,q] += i[c,p+r,q+s] * f[m,c,r,s]
How can we tell this is weight stationary?
Top loops are r and s

## Slide 8: CONV-layer Einsum
Traversal order (fastest to slowest):
Q, P, S, R
Parallel Ranks:
C, M

## Slide 9: NVDLA (Simplified) - Animation
M = 2
C = 2
R = 3
S = 3
H = 4
W = 8
P = 2
Q = 6
Notes: Weights are stationary in each PE
Input activations are “multi-cast” to contribute to multiple outputs
Multiple MAC results are combined in same cycle to contribute to an output
Output is not completed in a single cycle
Note every filter weight read in a cycle contributes to exactly one output in that cycle so for a particular weight there is a position in the sliding window that has the same shape as the output.